## Slide 1: Lecture 2 Recap

## Slide 2: SNMPv2 - Operations
Get - retrieve specific objects
Get-Next - retrieve objects by traversing a MIB tree
Set - modify or create objects
Get-Bulk - for bulk retrieval of objects
Trap - traps can be specified using object identifiers
Inform - acknowledged trap

## Slide 3: SNMPv2 – Get Bulk
Bulk retrieval of a table
The Get Bulk request has a variable binding list and 2 additional values:
  a non-repeaters value, and
  a max-repetitions value
A “GetBulkRequest ( non-repeaters=1, max-repetitions=2, varbindlist={sysUpTime, ifInOctets} )” will return:
  sysUpTime.0 1233413
  ifInOctets.1 345322
  ifInOctets.2 9981
If there is no lexicograhic successor, a value of “endOfMibView” will be returned

## Slide 4: SNMPv2 Message – Get Bulk
type
type:
0xA5 – SNMPv2 Get-Bulk request
- n is the non-repeaters value.
m is the max-repetitions value
the first ‘n’ variables (in variable bindings) will be retrieved by a single get-next iteration.
the rest of the variables will go through as many as m get-next iterations.
SNMPv2 Get-Bulk PDU:
m
Variable bindings
n
reqid

## Slide 5: SNMPv2 – Trap
SNMPv2 Trap PDU is identical to that of a Get, Get-Next, or Set PDU
The variable bindings specify information about the trap
  First variable provides agent’s sysUpTime when the trap was generated
  Second variable identifies what type of trap it is
  Additional variables based on the trap type
  A variable bindings in a linkDown trap will be:
    sysUpTime.0 32216671
    sysTrapOID.0 snmpTraps.3
    ifIndex.4 4
    ifAdminStatus.4 up
    ifOperStatus.4 down

## Slide 6: SNMPv2 Message - Trap
type
type:
0xA7 – SNMPv2 Trap
- Identical to that of a Get, Get-Next, and Set PDU
Generic traps defined in SNMPv1 has object identifiers in SNMPv2
SNMPv2 Trap PDU:
0
Variable bindings
0
reqid

## Slide 7: SNMPv2 Message - Inform
type
type:
0xA6 – SNMPv2 Inform request
- Identical to that of a Trap PDU
Inform response PDU has the same request identifier and variable bindings
SNMPv2 Inform PDU:
0
Variable bindings
0
reqid

## Slide 8: SMIv2 Managed Object Definition
A textual name along with its OBJECT IDENTIFIER.
SYNTAX clause
  Adds BITS construct: represents enumeration of named bits.
DESCRIPTION clause
MAX-ACCESS replacing ACCESS clause
  One of read-only, read-write, read-create, write-only, not-accessible or accessible-for-notify.
STATUS clause
  One of current, obsolete or deprecated
NOTIFICATION-TYPE Macro for defining SNMPv2 Traps.
AUGMENTS clause
  used to add additional columns to an existing table.
UNITS clause: optional clause
  contains the textual definition of the units associated with an object.
REFERENCE optional clause
  contains textual cross reference to an external MIB object.
DEFVAL optional clause provides a default value for the MIB object

## Slide 9: SMIv2 – BITS Construct
pmSchedWeekDay OBJECT-TYPE
SYNTAX BITS { sunday(0), monday(1), tuesday(2), wednesday(3), thursday(4), friday(5), saturday(6) }
MAX-ACCESS read-create
STATUS current
DESCRIPTION
"Within the overall time period specified in the pmSchedTimePeriod object, the value of this object specifies the specific days of the week within that time period when the schedule is active. Setting all bits will cause the schedule to act independently of the day of the week."
DEFVAL { { sunday, monday, tuesday, wednesday, thursday, friday, saturday } }
::= { pmSchedEntry 7 }

## Slide 10: SMIv2 Module Identity
ifMIB MODULE-IDENTITY
LAST-UPDATED "200006140000Z"
ORGANIZATION "IETF Interfaces MIB Working Group"
CONTACT-INFO " Keith McCloghrie Cisco Systems, Inc. 170 West Tasman Drive San Jose, CA 95134-1706 US 408-526-5260 kzm@cisco.com"
DESCRIPTION "The MIB module to describe generic objects for network interface sub-layers. This MIB is an updated version of MIB-II's ifTable, and incorporates the extensions defined in RFC 1229."
REVISION "200006140000Z"
DESCRIPTION "Clarifications agreed upon by the Interfaces MIB WG, and published as RFC 2863."
REVISION "199602282155Z"
DESCRIPTION "Revisions made by the Interfaces MIB WG, and published in RFC 2233."
::= { mib-2 31 }

## Slide 11: SMIv2 – Notification Type
linkDown NOTIFICATION-TYPE
OBJECTS {ifIndex, ifAdminStatus, ifOperStatus}
ACCESS read-only
STATUS current
DESCRIPTION
"A linkDown trap signifies that the SNMPv2 entity, acting in an agent role, has detected that the ifOperStatus object for one of its communication links is about to transition into the down state from some other state. This other state is indicated by the included value of ifOperStatus.”
::= { snmpTraps 3 }

## Slide 12: SMIv2 – Augments Clause
ifXTable OBJECT-TYPE
SYNTAX SEQUENCE OF IfXEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION "A list of interface entries. The number of entries is given by the value of ifNumber. This table contains additional objects for the interface table."
::= { ifMIBObjects 1 }
ifXEntry OBJECT-TYPE
SYNTAX IfXEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION "An entry containing additional management information applicable to a particular interface."
AUGMENTS { ifEntry }
::= { ifXTable 1 }

## Slide 13: SMIv2 Abstract Data Types
Integer32
  Same as an INTEGER
Counter32
  Same as a Counter
Gauge32
  Same as a Gauge
Unsigned32
  Same as a Gauge32
Counter64
  IMPLICIT INTEGER, 64-bit non-negative integer (0..264-1)
  Used to measure values that wrap in less than an hour with 32-bit counters.
DisplayString
  Resolves into an OCTET STRING
  Management information that represents text

## Slide 14: SMIv2 – Textual Conventions (contd.)
MacAddress
  Represents an 802 MAC address
  Resolves into a 6 byte OCTET STRING
TruthValue
  Resolves into an INTEGER
  Represents a boolean value of either true (1) or false (2)
TimeStamp
  Resolves into an TimeTicks
  Value of ‘sysUpTime’ when a specific occurrence happened
RowPointer
  Resolves into an OBJECT IDENTIFIER
  Pointer to a conceptual row
TestAndIncr
  Resolves into an INTEGER
  Used to prevent 2 or more management stations from trying to modify the same management information at the same time.

## Slide 15: SMIv2 – Textual Conventions
RowStatus
  Resolves into an INTEGER
  Provides a standard way to add or delete rows from a table
  Enumerated: {active (1), notInService (2), notReady (3), createAndGo (4), createAndWait (5), destroy (6)}
StorageType
  Resolves to an INTEGER
  Standard way to specify how a row should be stored in memory
  Enumerated: {other (1), volatile (2), nonVolatile (3), permanent (4), readOnly (5)}

## Slide 16: MIB-II Groups’ Newer Versions
System & SNMP Groups
  SNMPv2 MIB (RFC 3418)
Interfaces Group
  IF-MIB (RFC 2863),
IP Group
  IP-MIB (RFC 4293)
  IP-FORWARD-MIB (RFC 2096)
TCP Group
  TCP-MIB (RFC 4022)
UDP Group
  UDP-MIB (RFC 4113)

## Slide 17: System Group Changes
Defined in RFC 3418
Contains a new table object, sysORTable, and a new scalar object, sysORLastChange
  sysORTable ::= {system 9}, describes SNMPv2 entity’s support of various MIB modules and has 4 objects defined.
    sysORIndex,
    sysORID,
    sysORDescr, and
    sysORUpTime
  sysORLastChange ::= {system 8}, contains the value of sysUpTime when sysORTable was last changed.

## Slide 18: SNMP Group Changes
Defined in RFC 3418
snmpTrap ::=
internet.snmpV2.snmpModules.snmpMIB.snmpObjects.4
snmpTrapOID ::= {snmpTrap 1}
snmpTrapEnterprise ::= {snmpTrap 3}
snmpTraps ::= internet.snmpV2.snmpModules.snmpMIB.snmpObjects.5
  coldStart ::= {snmpTraps 1}
  warmStart ::= {snmpTraps 2}
  linkDown ::= {snmpTraps 3}
  linkUp ::= {snmpTraps 4}
  authenticationFailure ::= {snmpTraps 5}
  egpNeighborLoss ::= {snmpTraps 6}

## Slide 19: IF-MIB
RFC 2863
Rewrites IF group of MIB-II using SMIv2
ifMib ::= {mib-2 31}
ifMibObjects ::= {ifMib 1}
Defines 4 tables:
  ifTable ::= {interfaces 2}
  ifXTable ::= {ifMibObjects 1}
  ifStackTable ::= {ifMibObjects 2}
  ifRcvAddressTable ::= {ifMibObjects 4}

## Slide 20: IF-MIB
ifTable
  ifType has been redefined to be of IANAifType.
  Interfaces not restricted to 1 through the value of ifNumber.
  Adds a new scalar object ‘ifTableLastChange’
ifXTable
  Extension to the ifTable.
  Additional management information pertaining to a particular interface.
  Separate broadcast and multicast counters.
  High Capacity 64-bit counters.
    Supports interface speeds greater than 2.2 Gbps
  Deprecates several objects in the ifTable (ifInNUcastPkts, ifOutNUcastPkts, ifSpecific, ifOutQLen)

## Slide 21: ifXTable – 64-bit Counters