## Slide 1: Network & Service Management Summer 2015 Lecture 1 – Introduction to SNMP

## Slide 2: Network Management Elements
Consists of Managers and Agents.
  Managers (or Management Stations)
    Employ automatic or user initiated polling of managed devices.
  Agents
    Gather and store information about the managed resources
    Provide information to Managers on demand.
    Send alerts to Managers when events of interest occur.

## Slide 3: Network Management Framework
An overall architecture
  Consisting of manager(s) and managed devices.
A repository of managed objects
  Management Information Base (MIB)
Mechanism for describing and naming managed objects and events.
  Structure of Management Information (SMI)
Protocol for transferring management information.
  Simple Network Management Protocol (SNMP)
A number of general-purpose/standard MIBs.

## Slide 4: Management Information Base

## Slide 5: Network Management Architectures
Centralized
Weakly
Distributed
Strongly
Distributed

## Slide 6: ISO Standardization
ISO WG 4
http://www.iso.org
Defined the OSI Network Management Model
  Management should be powerful
  Object oriented approach
  Reliable exchange of management information
  CMIP, MIT

## Slide 7: OSI Management Model
Functional Component (FCAPS)
  Fault Management
  Configuration Management
  Accounting Management
  Performance Management
  Security Management
Information Component
  Management Information Tree (MIT)
Communication Component
  Common Management Information Protocol (CMIP)

## Slide 8: OSI Functional Component
Fault Management
  Detection and recovery of network anomalies and failures.
Configuration Management
  Provision network resources and services.
Accounting Management
  Collect usage data for the resources used; generate associated tariff.
Performance Management
  Monitor performance parameters, collect traffic statistics.
Security Management
  prevention and detection of improper access/use of network resources and services

## Slide 9: ITU-T Standardization
Defined the TMN framework
  Uses OSI Network Management Model
  Recommends out-of-band management.
  Support for Operations, Administration, Maintenance, and Provisioning (OAMP) of Telecommunications networks
  Logically separate network and interfaces with the Telecommunications network at several distinct point
http://www.itu.int/itu-t

## Slide 10: TMN Logical Layers
Network
Elements
Element Management
Network Management
Service Management
Business Management

## Slide 11: IETF Standardization
O&M Working Group
http://www.ietf.org
Defined the SNMP Management Standard
  Management should be simple
  Variable oriented approach
  Management information exchanges may be unreliable
  SNMPv1, SNMPv2c, SNMPv3
  SMI, MIB

## Slide 12: IETF Core SNMP RFCs
SNMP Protocol Specification
  Version 1 – RFC 1157
  Version 2 – RFCs 1901, 1902, 1903, 1904, 1905, 1906, 1907
  Version 3 – RFCs 3411, 3412, 3413, 3414, 3415
SMI
  Structure and identification of management information.
  SMIv1 - RFC 1155
  SMIv2 – RFC 2578
MIB-II
  Managed Object definitions for TCP/IP-based internets – RFC 1213
A large number of RFCs for IETF standard MIBs

## Slide 13: SNMP Management Framework
Link Layer
IP
UDP
SNMP
Get
Set
GetNext
GetResponse
Trap
Management
Application
Management Station
Link Layer
IP
UDP
SNMP
Get
Set
GetNext
GetResponse
Trap
Managed Device
Managed Objects (MIB)
Managed Resources
SNMP Messages
Application
Manages Objects

## Slide 14: A Typical SNMP Agent
Implements full SNMP protocol
Stores and retrieves management data as defined by the Management Information Base
Asynchronously signals events to a manager

## Slide 15: A Typical SNMP Manager
Implements full SNMP protocol
Able to:
  Query agents
  Get responses from agents
  Set variables in agents
  Acknowledge certain asynchoronous events from agents

## Slide 16: Structure of Management Information (SMI)
SMI specifies a set of rules for defining managed objects.
  RFC 1155 specifies SMIv1
  RFC 2578 specifies SMIv2
All managed objects are arranged in a hierarchical tree structure.
An object’s location in this tree structure identifies how to access this object

## Slide 17: SMIv1 Managed Object Definition
An Object type definition consists of five fields:
  A textual name with its corresponding OBJECT IDENTIFIER.
  SYNTAX, the object data type:
    Uses a subset of the ASN.1 notation
    Must resolve to a primitive data type (INTEGER, OCTET STRING, OBJECT IDENTIFIER)
  Access, how the object may be accessed (read-only, read-write, write-only, or not-accessible)
  Status, implementation requirement (mandatory, optional, or obsolete)
  Definition, textual description of the object type.

## Slide 18: SMIv1 Primitive Data Types
SYNTAX defines the data type for objects
Only the following ASN.1 primitive data types are permitted:
  INTEGER
  OCTET STRING
  OBJECT IDENTIFIER
Enumerated INTEGERs are allowed
ASN.1 type SEQUENCE is permitted for defining tables:
  SEQUENCE OF <entry>, where <entry> resolves to a list.

## Slide 19: SMIv1 Managed Object Definition
sysObjectID OBJECT-TYPE
SYNTAX OBJECT-IDENTIFIER
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The vendor's authoritative identification of the network management subsystem contained in the entity. This value is allocated within the SMI enterprises subtree (1.3.6.1.4.1)and provides an easy and unambiguous means for determining `what kind of box' is being managed.”
::= { system 2 }

## Slide 20: SMIv1 Abstract Data Types
IpAddress
  IMPLICIT OCTET STRING (SIZE(4))
  4-byte OCTET STRING
TimeTicks (hundredths of seconds)
  IMPLICIT INTEGER
  32-bit non-negative integer (0..232-1)
  Wraps around every 497 days
Counter (this wraps)
  IMPLICIT INTEGER
  32-bit non-negative integer (0..232-1)
Gauge (this doesn’t wrap)
  IMPLICIT INTEGER
  32-bit non-negative integer (0..232-1)

## Slide 21: SMIv1 Managed Object Definition
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the network management portion of the system was last re-initialized."
::= { system 3 }

## Slide 22: SMIv1 Managed Object Definition
ifTable OBJECT-TYPE
SYNTAX SEQUENCE OF IfEntry
ACCESS not-accessible
STATUS mandatory
DESCRIPTION
"A list of interface entries. The number of entries is given by the value of ifNumber."
::= { interfaces 2 }
ifEntry OBJECT-TYPE
SYNTAX IfEntry
ACCESS not-accessible
STATUS mandatory
DESCRIPTION
"An interface entry containing objects at the subnetwork layer and below for a particular interface."
INDEX { ifIndex }
::= { ifTable 1 }

## Slide 23: SMIv1 Managed Object Definition
IfEntry ::= SEQUENCE {
ifIndex
INTEGER,
ifDescr
DisplayString,
ifType
INTEGER,
ifMtu
INTEGER,
ifSpeed
Gauge,
...
}
ifDescr OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-only
STATUS mandatory
DESCRIPTION
"A textual string containing information about the interface. This string should include the name of the manufacturer, the product name and the version of the hardware interface."
::= { ifEntry 2 }

## Slide 24
iso (1)
org (3)
dod (6)
internet (1) IAB
directory (1)
mgmt (2) IANA
experimental (3) IANA
private (4) IANA
[iso org (3) dod (6)]
1.3.6
[iso org (3) dod (6) internet (1) mgmt (2)]
1.3.6.1.2
MIB Hierarchy
Not used

## Slide 25: The ‘mgmt’ node
The ‘mgmt (2)’ sub-tree is used to identify objects defined in IAB-approved documents
Administration of ‘mgmt (2)’ sub-tree delegated to IANA
When IETF/IAB approves a new Internet- standard Management Information Base (as an RFC), it is assigned an OBJECT IDENTIFIER by the IANA for identifying objects defined by that RFC.

## Slide 26: The ‘private’ sub-tree
Administration of the ‘private (4)’ sub-tree is delegated by the IAB to the IANA.
The ‘private (4)’ sub-tree is used to identify objects defined unilaterally.
This sub-tree has one child:
  enterprises OBJECT IDENTIFIER ::= { private 1 }
The ‘enterprises (1)’ sub-tree is used to permit enterprises to register their product models.
Upon receiving a sub-tree under ‘enterprises’, the enterprise define new MIB objects under this sub-tree.

## Slide 27: SNMPv1
First Internet management standard to be published
RFC 1157 published in 1990
Widely accepted and still the most common version of SNMP
SNMPv1 supports four operations
  Get, retrieve specific objects
  Get-Next, retrieve objects by traversing a MIB tree
  Set, modify or create objects
  Trap, send unsolicited notifications to management station(s).

## Slide 28: SNMPv1 - Get
Used to retrieve specific objects
A get-request for {sysUpTime.0, ifIndex.1, ifDescr.2} will return a response with variable bindings:
  sysUpTime.0 287231
  ifIndex.1 1
  ifDescr.2 ethernet
Only leaf objects can be retrieved
Retrieving non-leaf objects will result in a response with an error status of ‘noSuchName’

## Slide 29: SNMPv1 – Get-Next
Used to traverse the MIB tree
Retrieves the next leaf object in lexicographic order
A get-next request for {system, ifInUcastPkts.1, ifInNUcastPkts.1} will return a response with variable bindings:
  system.SysDecr.0 “router”
  ifInUcaastPkts.2 8876
  ifINNUcastPkts.2 1790
Non-leaf objects can be specified

## Slide 30: SNMPv1 – Set
Used to modify or create managed objects
The variable bindings specify object identifiers and the values to set them to.
Set operation is atomic – either all variables are set or none of them set.

## Slide 31: SNMPv1 – Traps
The coldStart Trap
The warmStart Trap
The linkDown Trap
The linkUp Trap
The authenticationFailure Trap
The egpNeighborLoss Trap
The enterpriseSpecific Trap

## Slide 32: SNMPv1 Message Structure
version
community
SNMP PDU
type
reqid
type:
0xA0 – GET
0xA1 – GETNEXT
0xA3 - SET
SNMP Request PDU:
SNMP Message Format:
Variable bindings
0
0

## Slide 33: SNMPv1 Message
type
reqid
type:
0xA2 – GET-RESPONSE
es (error-status):
noError (0)
tooBig (1)
noSuchName (2)
badValue (3)
readOnly (4)
genErr (5)
SNMP Response PDU:
es
ei
Variable bindings
ei (error-index):
Position of the first variable in the request that was in error

## Slide 34: SNMPv1 Trap Message
type
ent
type:
0xA4 – Trap
enterprise:
Device vendor (sysObjectId)
Agent address:
IP address of the device
Generic-trap:
1 of 6 generic traps
Specific-trap:
Enterprise specific trap
Timestamp:
Value of sysUpTime when the trap was generated
SNMP Trap PDU:
spec
gen
Variable bindings
addr
ts

## Slide 35: SNMPv1 - Trap PDU
Trap-PDU ::=
IMPLICIT SEQUENCE {
enterprise -- type of object generating trap
OBJECT IDENTIFIER,
agent-addr -- address of object generating trap
NetworkAddress,
generic-trap -- generic trap type
INTEGER {
coldStart(0),
warmStart(1),
linkDown(2),
linkUp(3),
authenticationFailure(4),
egpNeighborLoss(5),
enterpriseSpecific(6) },
specific-trap
INTEGER,
time-stamp
TimeTicks,
variable-bindings
VarBindList
}

## Slide 36: IETF MIB-2
MIB-2 is defined as iso.org.dod.internet.mgmt.1 (1.3.6.1.2.1)
Every device that supports SNMP MUST support MIB-2
Made up of nine groups
170 variables
Defines the variables to manage the TCP/IP protocol stack

## Slide 37
MIB-2 Subtree

## Slide 38
MIB-2 Groups
Subtree Name | OID | Description
System | 1.3.6.1.2.1.1 | Defines a list of objects that pertain to system operation, such as the system uptime, system contact, and system name.
Interfaces | 1.3.6.1.2.1.2 | Keeps track of the status of each interface on a managed entity (interfaces up/down, octets sent and received, errors and discards, etc. )
at | 1.3.6.1.2.1.3 | Network to physical address translation. (deprecated, exists for backward compatibility purposes)
ip | 1.3.6.1.2.1.4 | Tracks many aspects of IP, including IP routing.
icmp | 1.3.6.1.2.1.5 | Tracks things such as ICMP errors, discards, etc.
tcp | 1.3.6.1.2.1.6 | Tracks, among other things, the state of the TCP connection
udp | 1.3.6.1.2.1.7 | Tracks UDP statistics, datagrams in and out, etc.
egp | 1.3.6.1.2.1.8 | Tracks various statistics about the Exterior Gateway Protocol (EGP) and keeps an EGP neighbor table.
transmission | 1.3.6.1.2.1.10 | No objects are currently defined for this group, but other media-specific MIBs are defined using this subtree.
snmp | 1.3.6.1.2.1.11 | Measures the performance of the underlying SNMP implementation on the managed entity and tracks things such as the number of SNMP packets sent and received.