## Slide 1: CN8861 Network & Service Management Spring 2013
Govi Ravindran
Nishant Patel
Dept. of Electrical & Computer Engineering
Ryerson University

## Slide 2: Background
PhD (ECE), University of Toronto
Adjunct Faculty, ECE, Ryerson (’01-’08)
Teaching (‘05-’10)
Industrial experience (‘98-Present)
  Application Development
  Network Management Systems Design
  Telecom Services Design and Deployment

## Slide 3: Course Objective
Introduce Network Management concepts, technology, and tools.
Learn to specify, design, administer, and implement network management systems.
Prepare for jobs at Carriers, NEM, and MSOs.
Obtain vendor certifications.
http://www.cn.ryerson.ca/courses/8861.htm

## Slide 4: Course Overview
Detailed study of SNMP protocol and architectures.
Focuses on both agent and manager design.
Introduces commercial and open source network management tools.

## Slide 5: Course Outline
Introduction
  Building blocks
  Standardization & Framework
    The OSI Network Management Model
      CMIP, MIT, FCAPS
      FCAPS
    The Telecommunication Management Network (TMN) Framework
      Element, Network, Service Management
    IETF Management Framework
      SNMP, MIB, SMI

## Slide 6: Course Outline (contd.)
TCP/IP Management: SNMP Overview (v1, v2c)
  Evolution of SNMP Management standards
  SNMP Framework
  SNMP Protocol Messages (v1, v2c)
  Structure of Management Information (SMI)
  Management Information Base (MIB)
TCP/IP Management: SNMPv3
  SNMPv3 Message Format
  User Based Security Model (USM)
  View Based Access Control Model (VACM)
  SNMP Applications
  SNMPv3 MIB Modules

## Slide 7: Course Outline (contd.)
Tools
  HP Openview Network Node Manager
    Network Infrastructure Monitoring
    Integration Points
      Data Collection Configuration, Configuring Actions for Events, and Event Correlation
    Scalability, distributed management
  Net-SNMP Extensible Agent Development Kit
    Command Line Applications
  Nagios
    IT Infrastructure Monitoring

## Slide 8: Course Outline (contd.)
Advanced Topics
  Distributed Network Management Architectures
    Management by Delegation
      Script MIB (Delegation of Management Scripts)
      Schedule MIB (Scheduling Management Operations)
  SLA Management
  Agent Extension
  Event MIB
  Expression MIB

## Slide 9: Course Evaluation
20% - Assignment
  2 Assignments
30% - Midterm Quiz
  26th May
40% - Group Presentation
  9th June
10% - Class Participation

## Slide 10: Group Presentation
Research, design and present on a topic related to course material.
Example topics
  Tools (Nagios, SNMPc, MRTG, NNM)
  Data Center Management
  NETCONF
Groups of 3 or 4
Deliverables
  Presentation.
  Demonstration, if any.

## Slide 11: Useful Websites
http://www.simpleweb.org/
  RFCs, Tutorials, & Whitepapers
  Links to open source tools, research thesis
  Bibliography
http://www.ietf.org
  Operations & Management Working Group
http://www.net-snmp.org
  SNMP Agent toolkit
Vendor websites
  Cisco, HP

## Slide 12: References - Books
Douglas R. Mauro, Kevin J. Schmidt, “Essential SNMP”, O’Reilly
David Zeltserman, “A Practical Guide to SNMPv3 and Network Management”, Prentice Hall
David T. Perkins, Evan McGinnis, “Understanding SNMP MIBs”, Prentice-Hall

## Slide 13: RFC References – Lecture 1
SNMPv1
  RFC 1155, “Structure and Identification of Management Information (SMIv1) for TCP/IP based internets”.
  RFC 1157, “Simple Network Management Protocol”.
  RFC 1213, “Management Information Base for Network Management of TCP/IP internets: MIB-II”.

## Slide 14: Section 1 Introduction

## Slide 15: What is Network Management?
Network Management is a service that employs a variety of tools, applications, and devices to assist human network managers in monitoring and maintaining networks.

## Slide 16: Network Management Motivation
Why is it needed?
  In a perfect world, networks would not need management -they would just run themselves.
However…
  Parts tend to break
  Changes are made
  Somebody has to pay
  Performance below expectation
  Abuse happens
Management Areas
  Fault Management
  Configuration Management
  Accounting Management
  Performance Management
  Security Management

## Slide 17: Network Management Elements
Consists of Managers and Agents.
  Managers (or Management Stations)
    Employ automatic or user initiated polling of managed devices.
  Agents
    Gather and store information about the managed resources
    Provide information to Managers on demand.
    Send alerts to Managers when events of interest occur.

## Slide 18: Network Management Elements

## Slide 19: Management Information Base

## Slide 20: Network Management Architectures
Centralized
Weakly
Distributed
Strongly
Distributed

## Slide 21: Network Management Framework
An overall architecture
  Consisting of manager(s) and managed devices.
A repository of managed objects
  Management Information Base (MIB)
Mechanism for describing and naming managed objects and events.
  Structure of Management Information (SMI)
Protocol for transferring management information.
  Simple Network Management Protocol (SNMP)
A number of general-purpose/standard MIBs.

## Slide 22: Section 2 Network Management Standards

## Slide 23: Overview
International Organization for Standardization (ISO)
ITU Telecommunication Standardization Sector (ITU-T)
Internet Engineering Task Force (IETF)
Industry Consortiums
  Tele-Management Forum (TMF)

## Slide 24: ISO Standardization
ISO WG 4
http://www.iso.org
Defined the OSI Network Management Model
  Management should be powerful
  Object oriented approach
  Reliable exchange of management information
  CMIP, MIT

## Slide 25: OSI Management Model
Functional Component (FCAPS)
  Fault Management
  Configuration Management
  Accounting Management
  Performance Management
  Security Management
Information Component
  Management Information Tree (MIT)
Communication Component
  Common Management Information Protocol (CMIP)
  Common Management Information Service (CMIS)

## Slide 26: OSI Functional Component
Fault Management
  Detection and recovery of network anomalies and failures.
Configuration Management
  Provision network resources and services.
Accounting Management
  Collect usage data for the resources used; generate associated tariff.
Performance Management
  Monitor performance parameters, collect traffic statistics.
Security Management
  prevention and detection of improper access/use of network resources and services

## Slide 27: OSI Management Information Tree
Instances of Managed Objects (MO) organized in a hierarchical tree.
An unique Distinguishing Name (DN) identifies an MO instance.
DN is used by CMIP to identify and access managed information
State
Uptime
Location
Name
Diagnose
Start
Stop
Cold
Start
MO
Instance

## Slide 28: OSI Communication Component
MO Instances
Get/Set/Action
Event Notification
CMIP
CMIS
Attributes
Operations
Notifications
Agent
Event Forwarding
Event Detection
Selector

## Slide 29: OSI Communication Component
A
M
A
M
OSI
Protocol
Stack
Managed Objects
MIT
CMIP
CMIP
CMIS
System A
System B
System C
Operations/
Notifications
Operations/
Notifications

## Slide 30: CMIP Operations
M-INITIALIZE
  Establish Management Session
M-TERMINATE
  Terminate Management Session
M-ABORT
  Unconfirmed Termination
M-CREATE
  Creates an Instance MO instance
M-DELETE
  Deletes an MO instance

## Slide 31: CMIP Managed Information Exchange
M-GET
  Retrieve information
M-CANCEL-GET
  Cancel retrievals
M-SET
  Change an attribute value
M-ACTION
  Invoke an MO operation
M-EVENT-REPORT
  Generate an MO event report to a manager

## Slide 32: ITU-T Standardization
Defined the TMN framework
  Uses OSI Network Management Model
  Support for Operations, Administration, Maintenance, and Provisioning (OAMP) of Telecommunications networks
  Logically separate network for management and interfaces with the Telecommunications network at several distinct point
http://www.itu.int/itu-t

## Slide 33: TMN Logical Layers
Network
Elements
Element Management
Network Management
Service Management
Business Management

## Slide 34: IETF Standardization
IETF O&M Working Group
Defined the SNMP Management Standard
  Management should be simple
  Variable oriented approach
  Management information exchanges may be unreliable
  SNMPv1, SNMPv2c, SNMPv3
  SMI, MIB
http://www.ietf.org

## Slide 35: IETF Core SNMP RFCs
SNMP Protocol Specification
  Version 1 – RFC 1157
  Version 2 – RFCs 1901, 1902, 1903, 1904, 1905, 1906, 1907
  Version 3 – RFCs 3411, 3412, 3413, 3414, 3415
SMI
  Structure of Management Information.
  SMIv1 - RFC 1155
  SMIv2 – RFC 2578
MIB-II
  Managed Object definitions for TCP/IP-based internets – RFC 1213
IETF standard MIBs

## Slide 36: SNMP Management
Link Layer
IP
UDP
SNMP
Get
Set
GetNext
GetResponse
Trap
Management
Application
Management Station
Link Layer
IP
UDP
SNMP
Get
Set
GetNext
GetResponse
Trap
Managed Device
Managed Objects (MIB)
Managed Resources
SNMP Messages
Application
Manages Objects

## Slide 37: SNMP Proxy Management
Link Layer
IP
UDP
SNMP
Proxy Agent
Manager
Process
Link Layer
Proxy
Device
Protocol
Agent
Process
Link Layer
IP
UDP
SNMP
Agent Process
Link Layer
Mapping Function
Management
Station
Proxied
Device
Proxy
Device
Protocol

## Slide 38: SNMP Agent and Manager
A typical SNMP Agent
  Implements full SNMP protocol
  Stores and retrieves management data
  Asynchronously signals events to a manager
A typical SNMP Manager
  Implements full SNMP protocol
  Get response from agents
  Set variables in agents
  Receive events from agents

## Slide 39: IETF SNMP Standardization - Goal
Ubiquity
Inclusion of management should be inexpensive
  Small code
  Limited functionality
Management extensions should be possible
  New MIBs
Management should be robust
  Connectionless transport

## Slide 40: IETF SNMP Standardization - Reasons for Success
Rapid development of standards
Standards are obtained freely
Several prototypes demonstrating the feasibility of standards.

## Slide 41: Comparing Standardization Processes
Working
Document
Committee
Draft
Draft
Standard
Full
Standard
Technical Report
Technical Report
No Implementation
Required
No Implementation
Required
Working
Document
Proposed
Standard
Draft
Standard
Full
Standard
Historical
Historical
Implementation
Experience is a must
After a max of
2 years
Several Independent
Implementations must
Interwork
After a max of
4 years
ISO/OSI
IETF

## Slide 42
Section 3 SNMP Managed Objects

## Slide 43: Management Information Base (MIB)
Managed objects are accessed via a virtual information store, referred to as the Management Information Base (MIB).
MIB also refers to a collection of definitions of managed object.
ASN.1 notation is used to define MIB objects data types and values
  ASN.1 does not specify how these objects are encoded into strings of ones and zeros. SNMP uses the Basic Encoding Rules (BER).

## Slide 44: Structure of Management Information (SMI)
SMI specifies a set of rules for defining managed objects.
  RFC 1155 specifies SMIv1
  RFC 2578 specifies SMIv2
All managed objects are arranged in a hierarchical tree structure.
An object’s location in this tree structure identifies how to access this object

## Slide 45: SMIv1 Managed Object Definition
An Object type definition consists of five fields:
  A textual name..
  SYNTAX, the object data type:
    Uses a subset of the ASN.1 notation
    INTEGER, OCTET STRING, or OBJECT IDENTIFIER
  ACCESS, how the object may be accessed
    read-only, read-write, write-only, or not-accessible
  STATUS, implementation requirement
    mandatory, optional, or obsolete
  DESCRIPTION, textual description of the managed object.

## Slide 46: SMIv1 Primitive Data Types
Only the following ASN.1 data types are permitted:
  INTEGER
  OCTET STRING
  OBJECT IDENTIFIER
Enumerated INTEGERs are allowed
SEQUENCE is permitted for defining tables:
  SEQUENCE OF <entry>, where <entry> resolves to a list.

## Slide 47: SMIv1 Managed Object Definition
ifNumber OBJECT-TYPE
SYNTAX INTEGER
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The number of network interfaces (regardless of their current state) present on this system."
::= { interfaces 1 }

## Slide 48: SMIv1 Managed Object Definition
sysObjectID OBJECT-TYPE
SYNTAX OBJECT-IDENTIFIER
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The vendor's authoritative identification of the network management subsystem contained in the entity. This value is allocated within the SMI enterprises subtree (1.3.6.1.4.1)and provides an easy and unambiguous means for determining `what kind of box' is being managed.”
::= { system 2 }

## Slide 49: SMIv1 Managed Object Definition
ifTable OBJECT-TYPE
SYNTAX SEQUENCE OF IfEntry
ACCESS not-accessible
STATUS mandatory
DESCRIPTION
"A list of interface entries. The number of entries is given by the value of ifNumber."
::= { interfaces 2 }
ifEntry OBJECT-TYPE
SYNTAX IfEntry
ACCESS not-accessible
STATUS mandatory
DESCRIPTION
"An interface entry containing objects at the subnetwork layer and below for a particular interface."
INDEX { ifIndex }
::= { ifTable 1 }

## Slide 50: SMIv1 Abstract Data Types
IpAddress
  IMPLICIT OCTET STRING (SIZE(4))
  4-byte OCTET STRING
TimeTicks (hundredths of seconds)
  IMPLICIT INTEGER
  32-bit non-negative integer (0..232-1)
  Wraps around every 497 days
Counter (this wraps)
  IMPLICIT INTEGER
  32-bit non-negative integer (0..232-1)
Gauge (this doesn’t wrap)
  IMPLICIT INTEGER
  32-bit non-negative integer (0..232-1)

## Slide 51: SMIv1 Managed Object Definition
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the network management portion of the system was last re-initialized."
::= { system 3 }

## Slide 52: SMIv1 Managed Object Definition
IfEntry ::= SEQUENCE {
ifIndex
INTEGER,
ifDescr
DisplayString,
ifType
INTEGER,
ifMtu
INTEGER,
ifSpeed
Gauge,
...
}
ifDescr OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-only
STATUS mandatory
DESCRIPTION
"A textual string containing information about the interface. This string should include the name of the manufacturer, the product name and the version of the hardware interface."
::= { ifEntry 2 }

## Slide 53: Textual Conventions
Similar to the abstract data type.
Each of the Textual Convention has more precise semantics and used for the convenience of humans reading the MIB module.
RFC 2579 – “Textual Conventions for SMIv2”
PhysAddress ::= TEXTUAL-CONVENTION
DISPLAY-HINT "1x:"
STATUS current
DESCRIPTION "Represents media- or physical-level addresses."
SYNTAX OCTET STRING

## Slide 54: Textual Conventions
DisplayString SYNTAX OCTET STRING (SIZE (0..255))
PhysAddress SYNTAX OCTET STRING
MacAddress SYNTAX OCTET STRING (SIZE (6))
TruthValue SYNTAX INTEGER {true (1), false (2)}
TestandIncr SYNTAX INTEGER (0..2147483647)
AutonomousType SYNTAX OBJECT IDENTIFIER
VariablePointer SYNTAX OBJECT IDENTIFIER
RowPointer SYNTAX OBJECT IDENTITFIER
RowStatus SYNTAX INTEGER { active (1),
notInService (2),
notReady (3),
createAndGo (4), createAndWait (5),
destroy (6) }

## Slide 55: SMIv1 Managed Object Definition
sysDescr OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-only
STATUS mandatory
DESCRIPTION
"A textual description of the entity. This value should include the full name and version identification of the system's hardware type, software operating-system, and networking software. It is mandatory that this only contain printable ASCII characters."
::= { system 1 }

## Slide 56
Section 4 SNMP MIB Hierarchy

## Slide 57: Object Identifier
Object Identifier is a means of identifying an object.
An Object Identifier is a sequence of numbers which traverse a global tree
The global tree consists of a root connected to a number of labeled nodes via edges. Each node may, in turn, have children of its own which are labeled. This process may continue to an arbitrary level of depth.
Administrative control of the nodes may be delegated as one traverses the tree.

## Slide 58
iso (1)
org (3)
dod (6)
internet (1) IAB
directory (1)
mgmt (2) IANA
experimental (3) IANA
private (4) IANA
[iso org (3) dod (6)]
1.3.6
[iso org (3) dod (6) internet (1) mgmt (2)]
1.3.6.1.2
MIB Hierarchy
Not used

## Slide 59: The ‘root’ node
The root node unlabeled, but has three children directly under it:
  one node is administrated by the International Telegraph and Telephone Consultative Committee, with label CCITT (0).
  another is administered by the International Organization for Standardization, with label ISO (1).
  and the third is jointly administered by the ISO and the CCITT, JOINT-ISO-CCITT (2).
ISO (1) node,
  ISO has designated one sub-tree for use by other international organizations, ORG (3).
    One of the subtrees under ORG is administered by the U.S. Department of Defense, DOD (6).

## Slide 60: The ‘internet’ sub-tree
DoD has allocated a node to the Internet community, to be administered by the Internet Architecture Board (IAB) as follows:
  internet OBJECT IDENTIFIER ::= { iso org(3) dod(6) 1 }
There following nodes present under internet sub-tree:
  directory OBJECT IDENTIFIER ::= { internet 1 }
  mgmt OBJECT IDENTIFIER ::= { internet 2 }
  experimental OBJECT IDENTIFIER ::= { internet 3 }
  private OBJECT IDENTIFIER ::= { internet 4 }
  security OBJECT IDENTIFIER ::= {internet 5}
  snmpV2 OBJECT IDENTIFIER ::= {internet 6}

## Slide 61: The ‘MGMT’ node
Identify objects defined in IETF approved documents
Administration of the sub-tree delegated to IANA
When IETF approves a new Internet standard Management Information Base (as an RFC), it is assigned an OBJECT IDENTIFIER by the IANA for identifying objects defined by that RFC.

## Slide 62: The PRIVATE sub-tree
Administration of the PRIVATE (4) sub-tree is delegated to the IANA.
Used to identify objects defined unilaterally.
This sub-tree has one child:
  enterprises OBJECT IDENTIFIER ::= { private 1 }
The ‘enterprises (1)’ sub-tree is used to permit enterprises to register their product models.
Upon receiving a sub-tree under ‘enterprises’, the enterprise define new MIB objects under this sub-tree.

## Slide 63
Section 5 SNMPv1

## Slide 64: SNMPv1
First Internet management standard published as RFC in 1998
RFC 1157 published in 1990
Widely accepted and the most common version of SNMP

## Slide 65: SNMPv1 - Operations
First Internet management standard
RFC 1157 published in 1990
Widely accepted and the most common version of SNMP
Supports four basic operations:
  Get, retrieve specific objects
  Get-Next, retrieve objects by traversing a MIB tree
  Set, modify or create objects
  Trap, send unsolicited notifications to management station(s).

## Slide 66: SNMPv1 - Get
Used to retrieve specific MIB objects
A get-request for {sysUpTime.0, ifIndex.1, ifDescr.2} will return a response with variable bindings:
  sysUpTime.0 287231
  ifIndex.1 1
  ifDescr.2 ethernet
Only leaf objects can be retrieved
Retrieving non-leaf objects will result in a response with an error status of ‘noSuchName’

## Slide 67: SNMPv1 – Get-Next
Used to traverse the MIB tree
Retrieves the next leaf object in lexicographic order
A get-next request for {system, ifInUcastPkts.1, ifInNUcastPkts.1} will return a response with variable bindings:
  system.SysDecr.0 “router”
  ifInUcaastPkts.2 8876
  ifINNUcastPkts.2 1790
Non-leaf objects can be specified

## Slide 68: SNMPv1 – Set
Used to modify or create managed objects
The variable bindings specify object identifiers and the values to set them to.
Set operation is atomic – either all variables are set or none of them set.

## Slide 69: SNMPv1 – Traps
Seven Generic Traps defined
The coldStart Trap
  A coldStart(0) trap signifies that the agent is restarting such that the agent's configuration or implementation may be altered.
The warmStart Trap
  A warmStart(1) trap signifies that the agent is reinitializing. Neither the agent configuration nor implementation is altered.
The linkDown Trap
  A linkDown(2) trap signifies that the agent recognizes a failure in one of the communication links. The Trap-PDU contains the name and value of the ifIndex instance for the affected interface.
The linkUp Trap
  A linkUp(3) trap signifies that the agent recognizes that one of the communication links has come up. The Trap-PDU contains the name and value of the ifIndex instance for the affected interface.

## Slide 70: SNMPv1 – Traps
The authenticationFailure Trap
  An authenticationFailure(4) trap signifies that the agent received a protocol message that is not properly authenticated.
The egpNeighborLoss Trap
  An egpNeighborLoss(5) trap signifies that an EGP neighbor for whom the sending entity was an EGP peer has been marked down. The Trap-PDU contains the name and value of the egpNeighAddr instance for the affected neighbor.
The enterpriseSpecific Trap
  A enterpriseSpecific(6) trap signifies that the agent recognizes that some enterprise-specific event has occurred. The specific-trap field identifies the particular trap.

## Slide 71: SNMPv1- PDU Types
-- protocol data units
PDUs ::= CHOICE {
get-request
PDU,
get-next-request
PDU,
get-response
PDU,
set-request
PDU,
trap
Trap-PDU }

## Slide 72: SNMPv1 Message Structure
version
community
SNMP PDU
type
reqid
type:
0xA0 – GET
0xA1 – GETNEXT
0xA3 - SET
SNMP Request PDU:
SNMP Message Format:
Variable bindings
0
0

## Slide 73: SNMPv1 – Variable Bindings
VarBind ::= {
name
OID,
value
ObjectSyntax
}
VarBindList ::= SEQUENCE OF
VarBind

## Slide 74: SNMPv1 Message
type
reqid
type:
0xA2 – GET-RESPONSE
es (error-status):
noError (0)
tooBig (1)
noSuchName (2)
badValue (3)
readOnly (4)
genErr (5)
SNMP Response PDU:
es
ei
Variable bindings
ei (error-index):
Position of the first variable in the request that was in error

## Slide 75: SNMPv1 Message
type
ent
type:
0xA4 – Trap
enterprise:
Device vendor (sysObjectId)
Agent address:
IP address of the device
Generic-trap:
1 of 6 generic traps
Specific-trap:
Enterprise specific trap
Timestamp:
Value of sysUpTime when the trap was generated
SNMP Trap PDU:
spec
gen
Variable bindings
addr
ts

## Slide 76: SNMPv1 - Trap PDU
Trap-PDU ::=
IMPLICIT SEQUENCE {
enterprise -- type of object generating trap
OBJECT IDENTIFIER,
agent-addr -- address of object generating trap
NetworkAddress,
generic-trap -- generic trap type
INTEGER {
coldStart(0),
warmStart(1),
linkDown(2),
linkUp(3),
authenticationFailure(4),
egpNeighborLoss(5),
enterpriseSpecific(6) },
specific-trap
INTEGER,
time-stamp
TimeTicks,
variable-bindings
VarBindList
}

## Slide 77
Section 6 MIB-2

## Slide 78: IETF MIB-2
Defines the variables to manage the TCP/IP protocol stack
Every device that supports SNMP MUST support MIB-2
Made up of nine groups and 170 variables
First tree under MGMT: {iso.org.dod.internet.mgmt.1} (1.3.6.1.2.1)

## Slide 79
MIB-2 Subtree

## Slide 80: MIB-2 Definitions
RFC1213-MIB DEFINITIONS ::= BEGIN
IMPORTS
mgmt, NetworkAddress, IpAddress, Counter, Gauge, TimeTicks FROM RFC1155-SMI
OBJECT-TYPE FROM RFC-1212;
mib-2 OBJECT IDENTIFIER ::= { mgmt 1 }
-- textual conventions
DisplayString ::= OCTET STRING
-- This data type is used to model textual information taken -- from the NVT ASCII character set.
-- By convention, objects -- with this syntax are declared as having SIZE (0..255)
PhysAddress ::= OCTET STRING
-- This data type is used to model media addresses. For many types of media, this will be in a binary representation.
-- For example, an ethernet address would be represented as a string of 6 octets.
-- groups in MIB-II
system OBJECT IDENTIFIER ::= { mib-2 1 }
interfaces OBJECT IDENTIFIER ::= { mib-2 2 }
at OBJECT IDENTIFIER ::= { mib-2 3 }
ip OBJECT IDENTIFIER ::= { mib-2 4 }
icmp OBJECT IDENTIFIER ::= { mib-2 5 }
tcp OBJECT IDENTIFIER ::= { mib-2 6 }
udp OBJECT IDENTIFIER ::= { mib-2 7 }
egp OBJECT IDENTIFIER ::= { mib-2 8 }
-- historical
-- cmot OBJECT IDENTIFIER ::= { mib-2 9 }
transmission OBJECT IDENTIFIER ::= { mib-2 10 }
snmp OBJECT IDENTIFIER ::= { mib-2 11 }

## Slide 81
MIB-2 Groups
Subtree Name | OID | Description
System | 1.3.6.1.2.1.1 | Defines a list of objects that pertain to system operation, such as the system uptime, system contact, and system name.
Interfaces | 1.3.6.1.2.1.2 | Keeps track of the status of each interface on a managed entity (interfaces up/down, octets sent and received, errors and discards, etc. )
at | 1.3.6.1.2.1.3 | Network to physical address translation. (deprecated, exists for backward compatibility purposes)
ip | 1.3.6.1.2.1.4 | Tracks many aspects of IP, including IP routing.
icmp | 1.3.6.1.2.1.5 | Tracks things such as ICMP errors, discards, etc.
tcp | 1.3.6.1.2.1.6 | Tracks, among other things, the state of the TCP connection
udp | 1.3.6.1.2.1.7 | Tracks UDP statistics, datagrams in and out, etc.
egp | 1.3.6.1.2.1.8 | Tracks various statistics about the Exterior Gateway Protocol (EGP) and keeps an EGP neighbor table.
transmission | 1.3.6.1.2.1.10 | No objects are currently defined for this group, but other media-specific MIBs are defined using this subtree.
snmp | 1.3.6.1.2.1.11 | Measures the performance of the underlying SNMP implementation on the managed entity and tracks things such as the number of SNMP packets sent and received.

## Slide 82: MIB-2 Groups’ Newer Versions
System Group
  SNMPv2 MIB (RFC 1907)
Interfaces Group
  IF-MIB (RFC 2863)
IP & ICMP Groups
  IP-MIB (RFC 2011)
TCP Group
  TCP-MIB (RFC 2012)
UDP Group
  UDP-MIB (RFC 2013)
SNMP Group
  SNMPv2 MIB (RFC 1907)