## Slide 1: Network Management SNMP v2 & v3 12 May 2015

## Slide 2: Overview – Lecture 2
SNMPv2
MIB-2 Enhancements
SNMPv3 Framwork

## Slide 3: RFC References – SNMPv2
RFC 3416, “Version 2 of the Protocol Operations of the Simple Network Management Protocol”.
RFC 2578, “Structure of Management Information Version 2 (SMIv2)”.
RFC 2579, “Textual Conventions for SMIv2”.

## Slide 4: SNMPv2 - Operations
Includes following SNMPv1 operations
Get, retrieve specific objects
Get-Next, retrieve objects by traversing a MIB tree
Set, modify or create objects
In addition, the following operations are specified:
Get-Bulk, for bulk retrieval of objects
SNMPv2 Trap, traps can be specified using object identifiers
Inform, acknowledged trap

## Slide 5: SNMPv2 – Get Bulk
Bulk retrieval of a table
The Get Bulk request has a variable binding list and 2 additional values:
  a non-repeaters value, and
  a max-repetitions value
A “GetBulkRequest ( non-repeaters=1, max-repetitions=2, varbindlist={sysUpTime, ifInOctets} )” will return:
  sysUpTime.0 1233413
  ifInOctets.1 345322
  ifInOctets.2 9981
If there is no lexicograhic successor, a value of “endOfMibView” will be returned

## Slide 6: SNMPv2 Message – Get Bulk
type
type:
0xA5 – SNMPv2 Get-Bulk request
- n is the non-repeaters value.
m is the max-repetitions value
the first ‘n’ variables (in variable bindings) will be retrieved by a single get-next iteration.
the rest of the variables will go through as many as m get-next iterations.
SNMPv2 Get-Bulk PDU:
m
Variable bindings
n
reqid

## Slide 7: SNMPv2 – Trap
SNMPv2 Trap PDU is identical to that of a Get, Get-Next, or Set PDU
The variable bindings specify information about the trap
  First variable provides agent’s sysUpTime when the trap was generated
  Second variable identifies what type of trap it is
  Additional variables are based on the trap type
  A variable bindings in a ‘linkdown’ trap will be:
    sysUpTime.0 32216671
    sysTrapOID.0 snmpTraps.3
    ifIndex.4 4
    ifAdminStatus.4 up
    ifOperStatus.4 down

## Slide 8: SNMPv2 Message - Trap
type
type:
0xA7 – SNMPv2 Trap
- Identical to that of a Get, Get-Next, and Set PDU
Generic traps defined in SNMPv1 has object identifiers in SNMPv2
SNMPv2 Trap PDU:
0
Variable bindings
0
reqid

## Slide 9: SNMPv2 Message - Inform
type
type:
0xA6 – SNMPv2 Inform request
- Identical to that of a Trap PDU
Inform response PDU has the same request identifier and variable bindings
SNMPv2 Inform PDU:
0
Variable bindings
0
reqid

## Slide 10: SMIv2
The SMI is divided into three parts:
  Module definitions are used to describe MIB modules using MODULE-IDENTITY macro.
  Object definitions are used to describe managed objects. An OBJECT-TYPE macro is used to convey the syntax and semantics of a managed object.
  Notification definitions are used to describe unsolicited transmissions of management events. A NOTIFICATION-TYPE macro is used to convey the syntax and semantics of a notification.
Defined in RFC 2578

## Slide 11: SMIv2 Module Identity
ifMIB MODULE-IDENTITY
LAST-UPDATED "200006140000Z"
ORGANIZATION "IETF Interfaces MIB Working Group"
CONTACT-INFO " Keith McCloghrie Cisco Systems, Inc. 170 West Tasman Drive San Jose, CA 95134-1706 US 408-526-5260 kzm@cisco.com"
DESCRIPTION "The MIB module to describe generic objects for network interface sub-layers. This MIB is an updated version of MIB-II's ifTable, and incorporates the extensions defined in RFC 1229."
REVISION "200006140000Z"
DESCRIPTION "Clarifications agreed upon by the Interfaces MIB WG, and published as RFC 2863."
REVISION "199602282155Z"
DESCRIPTION "Revisions made by the Interfaces MIB WG, and published in RFC 2233."
::= { mib-2 31 }

## Slide 12: SMIv2 Managed Object Definition
A textual name along with its OBJECT IDENTIFIER.
SYNTAX clause
  Adds BITS construct: represents enumeration of named bits.
DESCRIPTION clause
MAX-ACCESS replacing ACCESS clause
  One of read-only, read-write, read-create, not-accessible or accessible-for-notify.
STATUS clause
  One of current, obsolete or deprecated
NOTIFICATION-TYPE Macro: used for defining SNMPv2 Traps.

## Slide 13: SMIv2 Managed Object Definition (contd.)
AUGMENTS clause
  used to add additional columns to an existing table.
UNITS clause (optional)
  contains the textual definition of the units associated with an object.
REFERENCE (optional)
  contains textual cross reference to an external MIB object.
DEFVAL (optional)
  provides a default value for the MIB object

## Slide 14: SMIv2 – Augments Clause
ifXTable OBJECT-TYPE
SYNTAX SEQUENCE OF IfXEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION "A list of interface entries. The number of entries is given by the value of ifNumber. This table contains additional objects for the interface table."
::= { ifMIBObjects 1 }
ifXEntry OBJECT-TYPE
SYNTAX IfXEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION "An entry containing additional management information applicable to a particular interface."
AUGMENTS { ifEntry }
::= { ifXTable 1 }

## Slide 15: SMIv2 – Augments Clause (contd.)
IfXEntry ::= SEQUENCE {
    ifName DisplayString,
    ifInMulticastPkts Counter32,
    ifInBroadcastPkts Counter32,
    ifOutMulticastPkts Counter32,
    ifOutBroadcastPkts Counter32,
    ifHCInOctets Counter64,
    ifHCInUcastPkts Counter64,
    ifHCInMulticastPkts Counter64,
    ifHCInBroadcastPkts Counter64,
    ifHCOutOctets Counter64,
    ifHCOutUcastPkts Counter64,
    ifHCOutMulticastPkts Counter64,
    ifHCOutBroadcastPkts Counter64,
    ifLinkUpDownTrapEnable INTEGER,
    ifHighSpeed Gauge32,
    ifPromiscuousMode TruthValue,
    ifConnectorPresent TruthValue,
    ifAlias DisplayString,
    ifCounterDiscontinuityTime TimeStamp }

## Slide 16: SMIv2 – BITS Construct
Enumeration of named bits
  SYNTAX BITS { up (0), down (1), testing (2),reserved (3)}
Assigned non-negative, contiguous value, starting at zero
Only enumerated bits are present
Recommended no more than 128 bits used
Labels for the bits – up to 64 characters

## Slide 17: SMIv2 – BITS Construct
pmSchedWeekDay OBJECT-TYPE
SYNTAX BITS { sunday(0), monday(1), tuesday(2), wednesday(3), thursday(4), friday(5), saturday(6) }
MAX-ACCESS read-create
STATUS current
DESCRIPTION
"Within the overall time period specified in the pmSchedTimePeriod object, the value of this object specifies the specific days of the week within that time period when the schedule is active. Setting all bits will cause the schedule to act independently of the day of the week."
DEFVAL { { sunday, monday, tuesday, wednesday, thursday, friday, saturday } }
::= { pmSchedEntry 7 }

## Slide 18: SMIv2 – Notification Type
linkDown NOTIFICATION-TYPE
OBJECTS {ifIndex, ifAdminStatus, ifOperStatus}
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"A linkDown trap signifies that the SNMPv2 entity, acting in an agent role, has detected that the ifOperStatus object for one of its communication links is about to transition into the down state from some other state. This other state is indicated by the included value of ifOperStatus.”
::= { snmpTraps 3 }

## Slide 19: SMIv2 Abstract Data Types
SMIv2 defines the following additional data types:
  Integer32
    Same as an INTEGER
  Counter32
    Same as a Counter
  Gauge32
    Same as a Gauge
  Unsigned32
    Same as a Gauge32
  Counter64
    IMPLICIT INTEGER
    64-bit non-negative integer (0..264-1)
    Used to measure values that wrap in less than an hour with 32-bit counters.

## Slide 20: SMIv2 – Textual Conventions
DisplayString
  Resolves into an OCTET STRING
  Management information that represents text is typically defined as a DisplayString
PhysAddress
  Resolves into an OCTET STRING
  Represents a media or physical level address
MacAddress
  Resolves into a 6-byte OCTET STRING
  Represents an 802 MAC address
TruthValue
  Resolves into an INTEGER
  Represents to a boolean value of either true (1) or false (2)

## Slide 21: SMIv2 – Textual Conventions
TestAndIncr
  Resolves into an INTEGER
  Used to prevent 2 or more management stations from trying to modify the same management information at the same time.
AutonomousType
  Resolves to an OBJECT IDENTIFIER
  Define a MIB sub-tree or a particular type of hardware or protocol
VariablePointer
  Resolves into an OBJECT IDENTIFIER
  Pointer to a specific object instance
RowPointer
  Resolves into an OBJECT IDENTIFIER
  Pointer to a row

## Slide 22: SMIv2 – Textual Conventions
TimeStamp
  Resolves to TimeTicks
  Value of sysUpTime when a specific occurrence happened
TimeInterval
  Resolves to an INTEGER
  Represents a period of time measured in hundredths of seconds
  Maximum value of 248 days (21474836.47 seconds)
DateAndTime
  Resolves into an OCTET STRING (8- or 11-byte)
  Represents a date-time specification
  Display format: “2d-1d-1d,1d:1d:1d.1d,1a1d:1d”
  Jan 15, 1999, 1:30:15 PM EDT would be displayed as
    1999-1-15,13:30:15.0,-4:0

## Slide 23: SMIv2 – Textual Conventions
TAddress
  Resolves to an OCTET STRING
  Represents a transport address
    UDP Domain – 6-byte OCTET STRING (IP Address, UDP Port)
StorageType
  Resolves to an INTEGER
  Standard way to specify how a row should be stored in memory
  Enumerated:
    other (1)
    volatile (2)
    nonVolatile (3)
    permanent (4)
    readOnly (5)

## Slide 24: SMIv2 – Textual Conventions
RowStatus
  Resolves into an INTEGER
  Provides a standard way to add or delete rows from a table
  Enumerated
    active (1)
    notInService (2)
    notReady (3)
    createAndGo (4)
    createAndWait (5)
    destroy (6)

## Slide 25: SMIv2 – RowStatus
The RowStatus textual convention is used to manage the creation and deletion of conceptual rows and has six defined values:
`active‘ - the row is available for use by the managed device
`notInService‘ - the row exists in the agent, but is unavailable for use by the managed device
`notReady‘ - the row exists in the agent, but is missing information necessary in order to be available for use by the managed device (i.e., one or more required columns in the row have not been instantiated)
‘createAndGo‘ - written by a manager to create a new instance of a row and to have its status automatically set to active, making it available for use by the managed device
‘createAndWait‘ - written by a manager to create a new instance of a row but not make it available for use by the managed device
’destroy’ - written by a manager to delete the existing row.

## Slide 26: SMIv2 – RowStatus
When queried, an existing row has three states:
  ‘active’ – row available for use by the managed device,
  ‘notInService’ - row not available for use by the managed device, though the agent has sufficient information, or,
  ‘notReady’ - row not available for use by the managed device because the agent has insufficient information.

## Slide 27: Section 2 IETF MIB-2 Enhancements

## Slide 28: MIB-II Groups’ Newer Versions
System & SNMP Groups
  SNMPv2 MIB (RFC 3418)
Interfaces Group
  IF-MIB (RFC 2863),
IP Group
  IP-MIB (RFC 4293)
  IP-FORWARD-MIB (RFC 2096)
TCP Group
  TCP-MIB (RFC 4022)
UDP Group
  UDP-MIB (RFC 4113)

## Slide 29: System Group Changes
Defined in RFC 3418
Contains a new table object, sysORTable, and a new scalar object, sysORLastChange
  sysORTable ::= {system 9}, describes SNMPv2 entity’s support of various MIB modules and has 4 objects defined.
    sysORIndex,
    sysORID,
    sysORDescr, and
    sysORUpTime
  sysORLastChange ::= {system 8}, contains the value of sysUpTime when sysORTable was last changed.

## Slide 30: SNMP Group Changes
Defined in RFC 3418
Redefines original mib-2 SNMP group using SMIv2.
Defines ‘snmpTrap’ group with 2 objects:
  snmpTrapOID – object identifier of the trap being sent (second varbind in SNMPv2 Trap or Inform Request PDU).
  snmpTrapEnterprise – object identifier of the enterprise associated with the trap being sent (last varbind in SNMPv2 Trap or Inform Request PDU).
Defines ‘snmpTraps’ group to map SNMPv1 generic traps

## Slide 31: SNMP Group Changes
snmpTrap ::= internet.6.3.1.1.4
snmpTrapOID ::= {snmpTrap 1}
snmpTrapEnterprise ::= {snmpTrap 3}
snmpTraps ::= internet.6.3.1.1.5
  coldStart ::= {snmpTraps 1}
  warmStart ::= {snmpTraps 2}
  linkDown ::= {snmpTraps 3}
  linkUp ::= {snmpTraps 4}
  authenticationFailure ::= {snmpTraps 5}
  egpNeighborLoss ::= {snmpTraps 6}

## Slide 32: IF-MIB
RFC 2863
Rewrites IF group of MIB-II using SMIv2
ifMib ::= {mib-2 31}
ifMibObjects ::= {ifMib 1}
Defines 4 tables:
  ifTable ::= {interfaces 2}
  ifXTable ::= {ifMibObjects 1}
  ifStackTable ::= {ifMibObjects 2}
  ifRcvAddressTable ::= {ifMibObjects 4}

## Slide 33: IF-MIB
ifTable
  ifType has been redefined to be of IANAifType.
  Interfaces not restricted to 1 through the value of ifNumber.
  Adds a new scalar object ‘ifTableLastChange’
ifXTable
  Extension to the ifTable.
  Additional management information pertaining to a particular interface.
  Separate broadcast and multicast counters.
  High Capacity 64-bit counters.
    Supports interface speeds greater than 2.2 Gbps
  Deprecates several objects in the ifTable (ifInNUcastPkts, ifOutNUcastPkts, ifSpecific, ifOutQLen)

## Slide 34: ifXTable – 64-bit Counters

## Slide 35: ifStackTable
Allows virtual interfaces to be layered on top of physical interfaces.
Shows the relationship between different sub-layers of network interfaces.
It shows which sub-layers run on top of which other sub-layers, where each sub-layer corresponds to a conceptual row in the ifTable.
ifStackHigherLayer – value of ifIndex corresponding to the higher sub-layer
ifStackLowerLayer – value of ifIndex corresponding to the lower sub-layer

## Slide 36
Section 3 SNMPv3

## Slide 37: SNMPv3 - RFCs
RFC 3411, “An Architecture for Describing Simple Network Management Protocol Management Frameworks”.
RFC 3412, “Message Processing and Dispatching for the Simple Network Management Protocol”.
RFC 3413, “Simple Network Management Protocol Applications”.

## Slide 38: SNMPv3 Security Requirements
The principal threats against which a Security Model should protect include:
  Modification of Information
The modification threat of in-transit SNMP messages by an unauthorized entity to effect unauthorized management operations.
  Masquerade
Unauthorized management operations may be attempted by assuming the identity of another principal that has the appropriate authorizations.

## Slide 39: SNMPv3 Security Requirements
The secondary threats against which a Security Model should provide protection include:
  Message Stream Modification
  Messages may be maliciously re-ordered, delayed or replayed to an extent to effect unauthorized management operations.
  Disclosure
  Eavesdropping on the exchanges between SNMP engines.

## Slide 40: SNMPv3 Management Framework
SNMPv3 is SNMPv2 plus Administration and Security.
Proposes a modular architecture that can be easily extended.
Consists of :
  SNMP entities
    a SNMP engine
    a set of applications
  a new message format
  a security model, and
  an access control model.

## Slide 41: SNMP Entity
Each SNMP entity consists of an SNMP engine and one or more associated applications
There is a one-to-one association between an SNMP engine and the SNMP entity which contains it.

## Slide 42: SNMP Entity
Dispatcher
Message
Processing
Subsystem
Security
Subsystem
Access Control
Subsystem
Command
Generator
Command
Responder
Notification
Receiver
Notification
Originator
Proxy
Forwarder
Other
SNMP Entity
SNMP Engine (identified by snmpEngineID)
Applications

## Slide 43: SNMP Engine
An SNMP Engine provides services for:
  sending and receiving messages
  authenticating and encrypting/decrypting messages, and
  controlling access to managed objects.
SNMP Engine consists of the following subsystems:
  Dispatcher Subsystem
  Message Processing Subsystem
  Security Subsystem
  Access Control Subsystem
‘snmpEngineID’ is the unique and unambiguous identifier of both an SNMP Entity and the SNMP Engine it contains.

## Slide 44: SNMP Engine - Dispatcher
Responsible for sending and receiving SNMP messages to/from the network.
Determines the version of an SNMP message and interacts with the corresponding Message Processing Model.
Provides interface to SNMP applications:
  for delivery of a PDU to an application
  for the applications to send a PDU to a remote SNMP entity.

## Slide 45: SNMP Engine – Message Processing Subsystem
Responsible for:
  preparing messages for sending, and
  extracting data from received messages
Contains multiple Message Processing Models
Each Message Processing Model is specific to a particular version of an SNMP message and prepares and extracts version-specific message formats.

## Slide 46: SNMP Engine – Message Processing Subsystem
SNMPv3
Message Processing
Model
SNMPv1
Message Processing
Model
SNMPv2c
Message Processing
Model
Other
Message Processing
Model
Message Processing Subsystem

## Slide 47: SNMP Engine – Security Subsystem
The Security Subsystem provides security services such as:
  Authenticating messages, and
  Encrypting/decrypting messages for privacy
Contains one or more Security Models
A Security Model specifies
  the threats against which it protects, and
  the security protocols used to provide security services such as authentication and privacy.

## Slide 48: SNMP Engine – Security Subsystem
User-based
Security Model
Other
Security Model
Security Subsystem
Other
Security Model

## Slide 49: SNMPv3 Security Level
Every message has an associated security level.
SNMPv3 recognizes three levels of security:
  without authentication and without privacy (noAuthNoPriv)
  with authentication but without privacy (authNoPriv)
  with authentication and with privacy (authPriv)

## Slide 50: SNMP Engine – Access Control Subsystem
The Access Control Subsystem provides authorization services by means of one or more Access Control Models.
An Access Control Model defines a particular access decision function for computing access rights.

## Slide 51: SNMP Engine – Access Control Subsystem
View-based
Access Control Model
Other
Access Control Model
Access Control Subsystem
Other
Access Control Model

## Slide 52: SNMP Applications
SNMP applications make use of the services provided by the SNMP engine
The different types of applications include:
  command generators, which monitor and manipulate management data
  command responders, which provide access to management data,
  notification originators, which initiate asynchronous messages,
  notification receivers, which process asynchronous messages, and
  proxy forwarders, which forward messages between entities.

## Slide 53: SNMPv3 Command Generator Call Flow
Command
Generator
Dispatcher
Command
Generator
Command
Generator
Message Processing Model
Command
Generator
Security Model
sendPDU
prepareOutgoingMsg
generateRequestMsg
Send SNMP Request Msg to Network
Send SNMP Response Msg to Network
prepareDataElements
processIncomingMsg
processResponsePDU

## Slide 54: SNMPv3 Command Responder Call Flow
Command
Generator
Dispatcher
Command
Responder
Command
Generator
Message Processing Model
Command
Generator
Security Model
registerContextEngineID
processIncomingMsg
Receive SNMP Request Message from Network
Send SNMP Response Msg to Network
prepareDataElements
generateResponseMsg
returnResponsePDU
processPDU
prepareResponseMsg

## Slide 55: SNMPv3 Implementations
Traditional SNMP agent: An SNMP entity with command responder and notification originator applications
SNMP proxy agent: An SNMP entity with proxy forwarder application
SNMP mid-level managers: entities with command generator and notification receiver, plus command responder and notification originator applications
SNMP network management stations: entities with command generator, notification receiver and possibly other types of applications for managing a very large number of managed nodes

## Slide 56
Command Generator
Application
Notification Originator
Application
Notification Receiver
Application
PDU Dispatcher
Message Dispatcher
Transport Mapping
V2c MP
V1 MP
V3 MP
other MP
User-based Security
Model
Other Security
Model
Dispatcher
Message Processing
Subsystem
Security
Subsystem
SNMP Engine
SNMP Applications
SNMP Manager
SNMP Entity
UDP
Network

## Slide 57
Message Dispatcher
V2c MP
V1 MP
V3 MP
other MP
User-based Security
Model
Other Security
Model
Dispatcher
Message Processing
Subsystem
Security
Subsystem
SNMP Engine
SNMPv3 Agent
SNMP Entity
Command Responder
Application
Notification Originator
Application
Notification Receiver
Application
SNMP Applications
View-based Access Control Model
Other Access Control
Model
Access Control
Subsystem
PDU Dispatcher
Transport Mapping
UDP
Network

## Slide 58: SNMP Context
An SNMP context is a collection of management information
  An item of management information may exist in more than one context.
  An SNMP entity potentially has access to many contexts.
Often a context is a physical device or a logical device and is defined as a subset of a single SNMP entity.
The combination of a contextEngineID and a contextName unambiguously identifies a context within an administrative domain
To identify an individual item of management information, its contextName and contextEngineID must be identified in addition to its object type and its instance.

## Slide 59: SNMP Context
Dispatcher
Message Processing
Subsystem
Security Subsystem
Access Control
Subsystem
SNMP Entity (identified by snmpEngineID, for e.g.: '800002b804616263'H
(enterpise 696, string "abc") )
SNMP Engine (identified by snmpEngineID)
Command Responder Application (contextEngineID, e.g.: '800002b804616263'H)
Example Context Names:
Bridge1
Bridge2
Bridge3
Bridge MIB
Bridge MIB
Other MIB
MIB Instrumentation
Context
Context
Context

## Slide 60: SNMPv3 – Message Format
Contains
  Message Header
    msgVersion
    msgID
    msgMaxSize
    msgFlags
    msgSecurityModel
  Security Header
  SNMPv2 PDU (plain text or encrypted)

## Slide 61: SNMPv3 Message Format
contextName
msgVersion
msgID
msgMaxSize
msgFlags
msgSecurityModel
msgAuthoritativeEngineID
msgAuthoritativeEngineBoots
msgAuthoritativeEngineTime
msgUserName
msgAuthenticationParameters
msgPrivacyParameters
contextEngineID
PDU
Scoped PDU
(plaintext or encrypted)
Generated/Processed by User Security Model (USM)
Generated/Processed by Message Processing Model
scope of
encryption
scope of
authentication

## Slide 62: SNMPv3 – Message Format
msgVersion
  A value of 3 identifies the version of the message as an SNMPv3 message
msgID
  Used to coordinate request and response messages between two SNMP entities
  Similar to the reqID used within a PDU
msgMaxSize
  Indicates the maximum message size that the sender can support
  Used to determine how big a response to a request message can be
  Values range from 484 to 231-1

## Slide 63: SNMPv3 – Message Format
msgFlags
  Indicates the security level that the sender has applied to the message.
  The 3 bits defined are reportableFlag, authFlag, and the privFlag
msgSecurityModel
  An integer value which identifies the message security model that the sender used to generate the message.
  The receiver must use the same security model to perform security processing for the message.

## Slide 64: SNMP ScopedPDU
A scopedPDU is a block of data containing a contextEngineID, a contextName, and a PDU.
contextName
contextEngineID
PDU
Scoped PDU
(plaintext or encrypted)
scope of
encryption
USM Message Headers
SNMPv3 Message Headers

## Slide 65: SNMPv3 – Reports
Used for engine-to-engine communication
Processed by the SNMPv3 message processing model
Allows to report the following type of errors (to the sender) when processing a SNMP message:
  A response message could not be generated
  A message was received with the authFlag cleared and the privFlag set
  An error occurred while providing authentication and privacy services for an incoming message

## Slide 66: SNMPv3 – Reports
type
reqid
0
0
Variable bindings
The PDU type 0xA8 indicates a Report PDU
‘reqid’ consists of request identifier of the message that triggered
the Report
Variable bindings will contain a single object identifier and its value.
Used to determine the problem that the report is identifying.