## Slide 1: SNMPv3

## Slide 2: Overview – SNMPv3
SNMPv3
  Architecture
  Message Format
  Security
  Applications
  Textual Conventions
  MIBs

## Slide 3: SNMPv3 - RFCs
RFC 3411, “An Architecture for Describing SNMP Management Frameworks”.
RFC 3412, “Message Processing and Dispatching for the SNMP”.
RFC 3413, “SNMP Applications”.

## Slide 4: Section 1 SNMPv3 Architecture

## Slide 5: SNMPv3 Architecture
SNMPv3 is SNMPv2 plus Administration and Security.
  Proposes a modular architecture that can be easily extended.
  Consists of :
    SNMP entity
      a SNMP engine
      a set of applications
    a new message format
    a security model, and
    an access control model.

## Slide 6: SNMP Entity
An SNMP entity contains an SNMP engine and one or more associated applications:
  command responder and notification originator application
    Access to management information
    Agent function
  command generator and/or notification receiver application
    Manager function

## Slide 7: SNMP Entity
Dispatcher
Message
Processing
Subsystem
Security
Subsystem
Access Control
Subsystem
Command
Generator
Command
Responder
Notification
Receiver
Notification
Originator
Proxy
Forwarder
Other
SNMP Entity
SNMP Engine (identified by snmpEngineID)
Applications

## Slide 8: SNMP Engine
An SNMP Engine provides services for:
  sending and receiving messages
  authenticating and encrypting/decrypting messages, and
  controlling access to managed objects.
SNMP Engine consists of the following subsystems:
  Dispatcher Subsystem
  Message Processing Subsystem
  Security Subsystem
  Access Control Subsystem
‘snmpEngineID’ is the unique and unambiguous identifier of both an SNMP Entity and the SNMP Engine it contains.

## Slide 9: SNMP Engine - Dispatcher
Allows for concurrent support of multiple versions of SNMP messages in the SNMP engine.
It is responsible for
  (1) accepting protocol data units (PDUs) from applications for transmission over the network and delivering incoming PDUs to applications;
  (2) passing outgoing PDUs to the Message Processing Subsystem to prepare as messages, and passing incoming messages to the Message Processing Subsystem to extract the incoming PDUs;
  (3) sending and receiving SNMP messages over the network.

## Slide 10: SNMP Engine – Message Processing Subsystem
Responsible for:
  preparing messages for sending, and
  extracting data from received messages
Contains multiple Message Processing Models
Each Message Processing Model is specific to a particular version of an SNMP message and prepares or extracts version-specific message formats.

## Slide 11: SNMP Engine – Message Processing Subsystem
SNMPv3
Message Processing
Model
SNMPv1
Message Processing
Model
SNMPv2c
Message Processing
Model
Other
Message Processing
Model
Message Processing Subsystem

## Slide 12: SNMP Engine – Security Subsystem
The Security Subsystem provides security services such as:
  Authenticating messages, and
  Encrypting/decrypting messages for privacy
Contains one or more Security Models
A Security Model specifies
  the threats against which it protects, and
  the security protocols used to provide security services such as authentication and privacy.

## Slide 13: SNMP Engine – Security Subsystem

## Slide 14: SNMP Engine – Security Subsystem
User-based
Security Model
Other
Security Model
Security Subsystem
Other
Security Model

## Slide 15: SNMPv3 Security Level
Every message has an associated security level.
SNMPv3 recognizes three levels of security:
  without authentication and without privacy (noAuthNoPriv)
  with authentication but without privacy (authNoPriv)
  with authentication and with privacy (authPriv)

## Slide 16: SNMP Engine – Access Control Subsystem
The Access Control Subsystem provides authorization services by means of one or more Access Control Models.
An Access Control Model defines a particular access decision function for computing access rights.

## Slide 17: SNMP Engine – Access Control Subsystem
View-based
Access Control Model
Other
Access Control Model
Access Control Subsystem
Other
Access Control Model

## Slide 18: SNMP Context
An SNMP context is a collection of management information
  An item of management information may exist in more than one context.
  An SNMP entity potentially has access to many contexts.
Often a context is a physical or a logical device and is defined as a subset of a single SNMP entity.
The combination of a contextEngineID and a contextName unambiguously identifies a context.
To identify an individual item of management information, its contextName and contextEngineID must be identified in addition to its object type and its instance.

## Slide 19: SNMP Context
Dispatcher
Message Processing
Subsystem
Security Subsystem
Access Control
Subsystem
SNMP Entity (identified by snmpEngineID, for e.g.: '800002b804616263'H)
SNMP Engine (identified by snmpEngineID)
Command Responder Application (contextEngineID, e.g.: '800002b804616263'H)
Example Context Names:
Bridge1
Bridge2
Bridge3
Bridge MIB
Bridge MIB
Bridge MIB
MIB Instrumentation
Context
Context
Context

## Slide 20: Section 2 SNMPv3 Message Format

## Slide 21: SNMPv3 – Message Format
Contains
  Message Header
    msgVersion
    msgID
    msgMaxSize
    msgFlags
    msgSecurityModel
  Security Header
  SNMPv2 PDU (plain text or encrypted)

## Slide 22: SNMPv3 Message Format
contextName
msgVersion
msgID
msgMaxSize
msgFlags
msgSecurityModel
msgAuthoritativeEngineID
msgAuthoritativeEngineBoots
msgAuthoritativeEngineTime
msgUserName
msgAuthenticationParameters
msgPrivacyParameters
contextEngineID
PDU
Scoped PDU
(plaintext or encrypted)
Generated/Processed by User Security Model (USM)
Generated/Processed by Message Processing Model
scope of
encryption
scope of
authentication

## Slide 23: SNMPv3 – Message Format
msgVersion
  A value of 3 identifies the version of the message as an SNMPv3 message
msgID
  Used to coordinate request and response messages between two SNMP entities
  Similar to the reqID used within a PDU
msgMaxSize
  Indicates the maximum message size that the sender can support
  Used to determine how big a response to a request message can be
  Values range from 484 to 231-1

## Slide 24: SNMPv3 – Message Format
msgFlags
  Indicates the security level that the sender has applied to the message.
  The 3 bits defined are reportableFlag, authFlag, and the privFlag
msgSecurityModel
  An integer value which identifies the message security model that the sender used to generate the message.
  The receiver must use the same security model to perform security processing for the message.

## Slide 25: SNMP ScopedPDU
A scopedPDU is a block of data containing a contextEngineID, a contextName, and a PDU.
contextName
contextEngineID
PDU
Scoped PDU
(plaintext or encrypted)
scope of
encryption
USM Message Headers
SNMPv3 Message Headers

## Slide 26: SNMPv3 – Reports
Used for engine-to-engine communication
Processed by the SNMPv3 message processing model
Allows to report the following type of errors (to the sender) when processing a SNMP message:
  A response message could not be generated
  A message was received with the authFlag cleared and the privFlag set
  An error occurred while providing authentication or privacy services for an incoming message

## Slide 27: SNMPv3 – Reports
type
reqid
0
0
Variable bindings
The PDU type 0xA8 indicates a Report PDU
‘reqid’ consists of request identifier of the message that triggered
the Report
Variable bindings will contain a single object identifier and its value.
Used to determine the problem that the report is identifying.

## Slide 28: Section 3 SNMPv3 Security

## Slide 29: SNMPv3 Security Requirements
Has the message been altered?
Is the message coming from a valid user?
Has the message been delayed or replayed?
Can sensitive information be protected against eavesdroppers?
Is the user allowed to access MIB objects specified in the message?

## Slide 30: SNMPv3 Security Requirements
The principal threats against which a Security Model should provide protection include:
  Modification of Information
The modification threat of in-transit SNMP messages by an unauthorized entity to effect unauthorized management operations.
  Masquerade
Unauthorized management operations may be attempted by assuming the identity of someone who has appropriate authorizations.

## Slide 31: SNMPv3 Security Requirements
The secondary threats against which a Security Model should provide protection include:
  Message Stream Modification
  Messages may be re-ordered, delayed or replayed to an extent to effect unauthorized management operations.
  Disclosure
  Eavesdropping on the exchanges between SNMP engines.

## Slide 32: SNMPv3 – Security
Authoritative and Non-authoritative Entities
Security Parameters
Discovery of snmpEngineID
Message Timeliness
Key Management
USM MIB

## Slide 33: Authoritative & Non-Authoritative Entities
Authoritative entity is the one which
  receives and responds to requests
  generates notifications
Entity
Authoritative
Entity
Request
Response
Notification

## Slide 34: SNMPv3 – Security Parameters
Every SNMPv3 message contains security parameters.
The following are USM security parameters:
UsmSecurityParameters ::=
  SEQUENCE {
    msgAuthoritativeEngineID OCTET STRING
    msgAuthoritativeEngineBoots INTEGER
    msgAuthoritativeEngineTime INTEGER
    msgUserName OCTET STRING
    msgAuthenticationParameters OCTET STRING
    msgPrivacyParameters OCTET STRING
    }

## Slide 35: SNMPv3 – EngineID Discovery
USM mechanism allows a non-authoritative SNMP entity to learn the snmpEngineID of the authoritative engine.
The non-authoritative entity sends a Request message to the authoritative entity with
  A securityLevel of “noAuthNoPriv”
  A msgUserName of zero length
  A msgAuthoritativeEngineID of zero length
  A empty variable-bindings
The authoritative entity responds by sending a Report message with its snmpEngineID value in the msgAuthoritativeEngineID field

## Slide 36: SNMPv3 – EngineID Discovery
Request:
securityLevel = noAuthNoPriv
msgUserName = ‘’
msgAuthoritativeEngineID = ‘’
Variable-bindings = ‘’
Authoritative
Engine
Non-Authoritative
Engine
Report:
msgAuthoritativeEngineID = snmpEngineID for A
usmStatsUnknownEngineIDs = n
NA
A

## Slide 37: SNMPv3 - EngineBoots & EngineTime Discovery
Request:
msgAuthoritativeEngineID= snmpEngineID for A
msgUserName = a valid user name known by A
msgAuthoritativeEngineBoots = 0
msgAuthoritativeEngineTime = 0
Authoritative
Engine
Non-Authoritative
Engine
Report:
msgAuthoritativeEngineBoots = snmpEngineBoots for A
msgAuthoritativeEngineTime = snmpEngineTime for A
usmStatsNotInTimeWindows = n

## Slide 38: SNMPv3 – Timeliness
An authoritative engine will discard a message if:
  bootsA = 2147483647, or
  bootsNA and bootsA are not equal, or
  (bootsNA = bootsA) & |timeA – timeNA| > 150s)

## Slide 39: SNMPv3 – Timeliness
When a non-authoritative engine receives a message
  bootsA and timeA are determined from the msgAuthoritativeEngineBoots and msgAuthoritativeEngineTime fields
  If (bootsA > bootsNA) or (bootsA = bootsNA & timeA > timeNA) is true, then the non-authoritative engine will update its bootsNA and timeNA values.
A non-authoritative engine will discard a message if:
  bootsNA = 2147483647
  bootsNA > bootsA
  (bootsNA = bootsA) & ((timeNA – timeA) > 150s)

## Slide 40: SNMPv3 – Key Management
User name is mapped to a textual password:
  USM has proposed procedures to convert a password into
    a 16-byte OCTET STRING that can be used by the HMAC-MD5-96 authentication protocol, and
    a 20-byte OCTET STRING that can be used by the HMAC-SHA-96 authentication protocol.
A single password for each user irrespective of the number of SNMP entities in a network
Localized secret keys will be derived for a user for each authoritative entity.

## Slide 41: SNMPv3 – Password to Key Generation
  Take the user’s password as input and produce a string of length 220 octets to form digest0.
  If a 16-octet key is desired, take the MD5 hash of digest0 to form digest1.
  If a 20-octet key is desired, take the SHA-1 hash of digest0 to form digest1.
  The output is user’s key.

## Slide 42: SNMPv3 – Localized Key Generation
  Form the string digest2 by concatenating digest1, the authoritative engine’s snmpEngineID value, and digest1.
  If a 16-octet key is desired, take the MD5 hash of digest2.
  If a 20-octet key is desired, take the SHA-1 hash of digest2.
  The output is user’s localized key for an authoritative SNMP entity.

## Slide 43: SNMPv3 – Key Management (contd.)
Key values can be changed through SNMP
Steps involved in a remote key change operation:
  Generate a new password for a user
  Get the new localized key value
  Generate a ‘random’ 16-byte OCTET STRING
  Calculate a value ‘delta’ using previous and new key values:
  temp <- MD5 (oldkey + random)
  for (i = 0; i < 16; i++) {
  delta [i] = (temp [i]) XOR (newkey [i])
  }
  Concatenate ‘random’ and ‘delta’ to form a 32-byte OCTET STRING, which will be used to remotely configure an authoritative entity’s new secret key.

## Slide 44: SNMPv3 – Key Management (contd.)
A remote entity will calculate the new key value given ‘random’ and ‘delta’:
Note: if (a XOR b = c) then (a XOR c = b))
  temp <- MD5 (oldkey + random)
  for (i=0; i < 16; i++)
  {
  newkey [i] = temp [i] XOR delta[i]
  }

## Slide 45: SNMPv3 – Authentication MD5
16-byte secret authentication key
Create ‘extendedKey’ which is the secret authentication key appended with 48 zero octets.
The 12-octet MAC is computed as follows:
temp <- MD5 (K2 + MD5 (K1 + message)) // 16-byte octet string
MAC <- temp[0…11]
where K1 and K2 are computed as follows:
for (i = 0; i < 64; i++) {
K1 [i] = extendedKey [i] XOR 0x36
}
for (i = 0; i < 64; i++) {
K2 [i] = extendedkey [i] XOR 0x5C
}

## Slide 46: SNMPv3 – Authentication SHA
20-byte secret authentication key
Create ‘extendedKey’ which is the secret auth key appended with 44 zero octets.
The 12-octet MAC is computed as follows:
temp <- SHA (K2 + SHA (K1 + message)) // 16-byte octet string
MAC <- temp[0…11]
where K1 and K2 are computed as follows:
for (i = 0; i < 64; i++) {
K1 [i] = extendedKey [i] XOR 0x36
}
for (i = 0; i < 64; i++) {
K2 [i] = extendedkey [i] XOR 0x5C
}

## Slide 47: SNMPv3 – Privacy CBC-DES
Symmetric secret key algorithm
16-byte secret key
‘msgPrivacyParameters’ field will contain an 8-byte octet string that represents a ‘salt’ value for the initialization vector used in DES encryption.

## Slide 48: Section 4 SNMPv3 Applications

## Slide 49: SNMP Applications
SNMP applications make use of the services provided by the SNMP engine
The different types of applications include:
  command generators monitor and manipulate mgmt data
  command responders provide access to management data,
  notification originators initiate asynchronous messages,
  notification receivers process asynchronous messages, and
  proxy forwarders forward messages between entities.

## Slide 50: Command Generator Applications
Initiate SNMP Get, Get-Next, Get-Bulk, and Set requests and process responses to those requests
The request identifier from the response PDU should match what was used in the original request.
The response values of msgVersion, securityModel, contextEngineID, and contextName must match original request values.

## Slide 51: Command Responder Applications
Provide access to management data.
Process a request when the contextEngineID specified matches the local SNMP engine.
Perform appropriate operation and generate a response.
Each object in the request’s variable binding is tested to see if it can be accessed based on the MIB view.

## Slide 52: Notification Originator Application
Generates SNMPv2-Trap or Inform notification.
SNMPv3 defines MIB tables to configure the following:
  target address(es) to send notifications to,
  whether a SNMPv2-Trap or Inform PDU is sent, and
  what timeout and retry counts to use for Inform PDUs.

## Slide 53: Notification Receiver Application
Registers with the Dispatcher to receive SNMPv2-Trap and/or Inform PDUs.
When Inform PDU is received, a response is generated using the original request identifier and variable-bindings, setting the error-status and error-index to zero.

## Slide 54: SNMPv3 Command Generator Call Flow
Command
Generator
Dispatcher
Command
Generator
Command
Generator
Message Processing Model
Command
Generator
Security Model
sendPDU
prepareOutgoingMsg
generateRequestMsg
Send SNMP Request Msg to Network
Send SNMP Response Msg to Network
prepareDataElements
processIncomingMsg
processResponsePDU

## Slide 55: SNMPv3 Command Responder Call Flow
Command
Generator
Dispatcher
Command
Responder
Command
Generator
Message Processing Model
Command
Generator
Security Model
registerContextEngineID
processIncomingMsg
Receive SNMP Request Message from Network
Send SNMP Response Msg to Network
prepareDataElements
generateResponseMsg
returnResponsePDU
processPDU
prepareResponseMsg

## Slide 56: Proxy Forwarder Application
Forwards requests and/or notifications to other SNMP entities.
Forwards responses to the SNMP entity that sent the original message.
SNMPv3 defines MIB tables on how to map incoming message to one or more target addresses.

## Slide 57: Proxy Forwarder Application
Originator
Entity
Target
Entity
Proxy
Forwarder
Get, reqid = x
Get-Resp, reqid = x
Get, reqid = y
Get-Resp, reqid = y
Originator
Entity
Target
Entity
Proxy
Forwarder
Get, reqid = x
Report, reqid = x
Report, reqid = y
Get, reqid = y

## Slide 58: Proxy Forwarder Application
Originator
Entity
Target
Entity
Proxy
Forwarder
Inform, reqid = x
Response, reqid = x
Inform, reqid = y1
Target
Entity
Response, reqid = y1
Inform, reqid = y2
Response, reqid = y2

## Slide 59: SNMPv3 Implementations
Traditional SNMP agent: An SNMP entity with command responder and/or notification originator applications
SNMP proxy agent: An SNMP entity with proxy forwarder application
SNMP mid-level manager: An SNMP entity with command generator and/or notification receiver, plus command responder and/or notification originator applications
SNMP network management stations: entities with all SNMP applications and possibly other types of applications for managing a very large number of managed nodes

## Slide 60
Command Generator
Application
Notification Originator
Application
Notification Receiver
Application
PDU Dispatcher
Message Dispatcher
Transport Mapping
V2c MP
V1 MP
V3 MP
other MP
User-based Security
Model
Other Security
Model
Dispatcher
Message Processing
Subsystem
Security
Subsystem
SNMP Engine
SNMP Applications
SNMP Manager
SNMP Entity
UDP
Network

## Slide 61
Message Dispatcher
V2c MP
V1 MP
V3 MP
other MP
User-based Security
Model
Other Security
Model
Dispatcher
Message Processing
Subsystem
Security
Subsystem
SNMP Engine
SNMPv3 Agent
SNMP Entity
Command Responder
Application
Notification Originator
Application
Notification Receiver
Application
SNMP Applications
View-based Access Control Model
Other Access Control
Model
Access Control
Subsystem
PDU Dispatcher
Transport Mapping
UDP
Network

## Slide 62: Section 5 SNMPv3 Textual Conventions

## Slide 63: SNMPv3 – Textual Conventions
SnmpEngineID
  SNMP engine’s administratively assigned unique identifier.
    Used for identification and not for addressing.
    Resolves to an OCTET STRING between 5 and 32 bytes long
  The very first bit is used to indicate how the rest of the data is composed:
    ‘0’ - as defined by enterprise
    ‘1’ - as defined by standard architecture.

## Slide 64: SNMPv3 – Textual Conventions
SnmpEngineID Standard Definition
  The length of the octet string varies
  The very first bit is set to 1
  The first four octets are used for the private enterprise number.
  The fifth octet indicates how the rest (6th and following octets) are formatted:
  0 - reserved, unused.
  1 - IPv4 address (4 octets)
  2 - IPv6 address (16 octets)
  3 - MAC address (6 octets)
  4 - Text, administratively assigned (maximum length 27)
  5 - Octets, administratively assigned (maximum length 27)
  6-127 - reserved, unused
  128-255 - as defined by the enterprise (maximum length 27)

## Slide 65: SNMPv3 – Textual Conventions
SnmpEngineID Enterprise Definition
  Has a fixed length of 12 octets
  The very first bit is set to 0
  The first four octets are set to the private enterprise number
  The remaining eight octets are determined via one or more enterprise-specific methods. For example, it may be the IP address of the SNMP entity, or the MAC address of one of the interfaces.

## Slide 66: SNMPv3 – Textual Conventions
snmpSecurityModel
  Uniquely identifies a Security Model of the Security Subsystem
  Resolves to an INTEGER
    ‘0’, reserved for any.
    ‘1’, SNMPv1
    ‘2’, SNMPv2c
    ‘3’, User-Based Security Model (USM)
    4-255 reserved for future use
    Values greater than 255 are allocated to enterprise-specific Security Models as follows:
      enterpriseID * 256 + securityModel
    This allows enterprises to define up to 255 enterprise specific security models and up to 223-1 (8,388,606) enterprises

## Slide 67: SNMPv3 – Textual Conventions
snmpSecurityLevel
  Resolves to an INTEGER
  Defines the 3 security levels that can be used
  noAuthNoPriv (1)
  SNMP messages are sent without authentication and without privacy
  authNoPriv (2)
  SNMP messages are sent with authentication but without privacy
  authPriv (3)
  SNMP messages are sent with authentication and with privacy

## Slide 68: SNMPv3 – Textual Conventions
SnmpMessageProcessingModel
  Uniquely identifies the message processing model
  Resolves to an INTEGER:
    ‘0’, SNMPv1
    ‘1’, SNMPv2c
    ‘2’, SNMPv2u or SNMPv2*
    ‘3’, SNMPv3
    4-255, reserved for standards-track message processing models.
    Values greater than 255 are handled the same way as with the ‘snmpSecurityModel’:
    enterpriseID * 256 + messageProcessingModel
    This allows enterprises to define up to 255 message processing models.

## Slide 69: SNMPv3 – Textual Conventions
snmpAdminString
  Resolves to an OCTET STRING (Up to 255 bytes long)
  Used to represent administrative information in human readable form.
  Represents textual information such as a user name or an identifier string

## Slide 70: Section 6 SNMPv3 MIBs

## Slide 71: SNMP Local Configuration Datastore
The SNMP entity retains its own sets of configuration information.
Part of the configuration information is accessible via managed objects and is published in SNMPv3 MIBs.

## Slide 72: SNMPv3 MIBs
snmpModules
{snmpV2 3}
snmpMPDMIB
{snmpModules 11}
snmpUSMMIB
{snmpModules 15}
snmpTargetMIB
{snmpModules 12}
snmpFrameworkMIB
{snmpModules 10}
snmpNotificationMIB
{snmpModules 13}
snmpProxyMIB
{snmpModules 14}
snmpVACMMIB
{snmpModules 16}
snmpV2
{internet 6}
internet
{.iso.org.dod.1}

## Slide 73: SNMPv3 MIBs – Entity
SNMP-FRAMEWORK-MIB
  RFC 2571, “An Architecture for Describing SNMP Management Frameworks”
  {internet snmpV2 snmpModules 10}
SNMP-MPD-MIB
  RFC 2572, “Message Processing and Dispatching for the Simple Network Management protocol”
  {internet snmpV2 snmpModules 11}

## Slide 74: SNMPv3 – Framework MIB
snmpEngine
snmpEngineID
{snmpEngine 1}
snmpEngineTime
{snmpEngine 3}
snmpEngineBoots
{snmpEngine 2}
snmpEngineMaxMessageSize
{snmpEngine 4}
snmpFrameworkAdmin
{snmpFrameworkMIB 1}
snmpFramework MIB
{.iso.org.dod.internet.snmpV2.snmpModules 10}
snmpFrameworkMIBObjects
snmpFrameworkMIBConformances
{snmpFrameworkMIB 2}
{snmpFrameworkMIB 3}

## Slide 75: Framework MIB
snmpEngineID OBJECT-TYPE
SYNTAX SnmpEngineID
MAX-ACCESS read-only
STATUS current
DESCRIPTION "An SNMP engine's administratively-unique identifier. This information SHOULD be stored in non-volatile storage so that it remains constant across re-initializations of the SNMP engine. "
::= { snmpEngine 1 }
snmpEngineBoots OBJECT-TYPE
SYNTAX INTEGER (1..2147483647)
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The number of times that the SNMP engine has initialized itself since snmpEngineID was last configured. "
::= { snmpEngine 2 }

## Slide 76: Framework MIB
snmpEngineTime OBJECT-TYPE
SYNTAX INTEGER (0..2147483647)
UNITS "seconds"
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The number of seconds since the value of the snmpEngineBoots object last changed. When incrementing this object's value would cause it to exceed its maximum, snmpEngineBoots is incremented as if a re-initialization had occurred, and this object's value consequently reverts to zero. "
::= { snmpEngine 3 }
snmpEngineMaxMessageSize OBJECT-TYPE
SYNTAX INTEGER (484..2147483647)
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The maximum length in octets of an SNMP message which this SNMP engine can send or receive and process, determined as the minimum of the maximum message size values supported among all of the transports available and supported by the engine. "
::= { snmpEngine 4 }

## Slide 77: SNMPv3 – MPD MIB
snmpMPDStats
snmpInvalidMsgs
{snmpMPDStats 2}
snmpUnknownSecurityModels
{snmpMPDStats 1}
snmpUnknownPDUHandlers
{snmpMPDStats 3}
snmpMPDAdmin
{snmpMPDMIB 1}
snmpMPD MIB
{.iso.org.dod.internet.snmpV2.snmpModules 11}
snmpMPDMIBObjects
snmpMPDMIBConformances
{snmpMPDMIB 2}
{snmpMPDMIB 3}

## Slide 78: SNMPv3 – MPD Statistics
snmpUnknownSecurityModels OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The total number of packets received by the SNMP engine which were dropped because they referenced a securityModel that was not known to or supported by the SNMP engine. "
::= { snmpMPDStats 1 }
snmpInvalidMsgs OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The total number of packets received by the SNMP engine which were dropped because there were invalid or inconsistent components in the SNMP message. "
::= { snmpMPDStats 2 }
snmpUnknownPDUHandlers OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The total number of packets received by the SNMP engine which were dropped because the PDU contained in the packet could not be passed to an application responsible for handling the pduType, e.g. no SNMP application had registered for the proper combination of the contextEngineID and the pduType. “
::= { snmpMPDStats 3 }

## Slide 79: SNMPv3 Authentication & Privacy MIBs
snmpModules
{snmpV2 3}
snmpMPDMIB
{snmpModules 11}
snmpUSMMIB
{snmpModules 15}
snmpTargetMIB
{snmpModules 12}
snmpFrameworkMIB
{snmpModules 10}
snmpNotificationMIB
{snmpModules 13}
snmpProxyMIB
{snmpModules 14}
snmpVACMMIB
{snmpModules 16}
snmpV2
{internet 6}
internet
{.iso.org.dod.1}

## Slide 80: SNMPv3 MIBs – Authentication & Privacy
SNMP-USM-MIB
  RFC 2574, “User-based Security Model for version 3 of the Simple Network Management Protocol (SNMPv3)”
  {snmpModules 15}
SNMP-VACM-MIB
  RFC 2575, “View-based Access Control Model for the Simple Network Management Protocol”
  {snmpModules 16}

## Slide 81: SNMPv3 – USM MIB
usmUser
snmpUsm MIB
{.iso.org.dod.internet.snmpV2.snmpModules 15}
usmMIBObjects
usmMIBConformances
{snmpUsmMIB 1}
{snmpUsmMIB 2}
usmStats
usmUserSecurityName
usmUserCloneFrom
usmUserAuthProtocol
usmUserAuthKeyChange
usmUserOwnAuthKeyChange
usmUserPrivProtocol
usmUserPrivKeyChange
usmUserOwnPrivKeyChange
usmUserPublic
usmUserSpinLock
usmUserTable
usmUserStorageType
usmUserEngineID
usmStatsDecryptionErrors
usmUserStatus
usmStatsUnsupportedSecLevels
usmStatsNotInTimeWindows
usmStatsUnknownUserNames
usmStatsUnknownEngineIDs
usmStatsWrongDigests

## Slide 82: SNMPv3 – USM MIB
Defines a table of valid users for the User-based Security Model (usmUserTable)
Defines authentication and privacy protocols
Defines USM Error Statistics
A TestAndIncr object, ‘usmUserSpinLock’, used to coordinate ‘set’ operations to the usmUserTable

## Slide 83: SNMPv3 – USM MIB
usmUserAuthProtocol values defined so far:
Authentication Protocol | Value | Object Identifier
None | usmNoAuthProtocol | {snmpAuthProtocols 1}
HMAC-MD5-96 | usmHMACMD5AuthProtocol | {snmpAuthProtocols 2}
HMAC-SHA-96 | usmHMACSHAAuthProtocol | {snmpAuthProtocols 3}

## Slide 84: SNMPv3 – USM MIB
usmUserPrivProtocol values defined so far:
Authentication Protocol | Value | Object Identifier
None | usmNoPrivProtocol | {snmpPrivProtocols 1}
CBC-DES | usmDESPrivProtocol | {snmpPrivProtocols 2}

## Slide 85: SNMPv3 – USM User Table
Object
Type
Access
usmUserEngineID
usmUserName
usmUserSecurityName
usmUserCloneFrom
usmUserAuthProtocol
usmUserAuthKeyChange
usmUserOwnAuthKeyChange
usmUserPrivProtocol
usmUserPrivKeyChange
usmUserOwnPrivKeyChange
usmUserPublic
usmUserStorageType
usmUserStatus
SnmpEngineID
SnmpAdminString
SnmpAdminString
RowPointer
AutonomousType
KeyChange
KeyChange
KeyChange
KeyChange
AutonomousType
OCTET STRING
StorageType
RowStatus
not-accessible
not-accessible
read-only
read-create
read-create
read-create
read-create
read-create
read-create
read-create
read-create
read-create
read-create

## Slide 86: SNMPv3 – USM User Table
‘usmUserTable’ maintains authentication and privacy information for each user
Each user is indexed by an SNMP engine identifier and a user name
The SNMP engine identifier is mostly local but remote engine identifiers can exist
Each row specifies the authentication protocol and the encryption protocol to use when exchanging SNMP messages for a specific user
Each row also contains authentication and encryption KeyChange objects to allow secret keys to be changed remotely

## Slide 87: SNMPv3 – USM User Table
New rows in the usmUserTable are created by cloning them from existing rows
Atleast one template row must be created and have its secret keys configured through some means other than SNMP (through a command line interface) so that the new rows can be cloned from it.

## Slide 88: SNMPv3 – USM Error Statistics
usmStatsUnsupportedSecLevels
  32-bit Counter
  Number of packets dropped because of the requested security level is not supported.
usmStatsNotInTimeWindows
  32-bit Counter
  Number of packets dropped because they were outside an authoritative engine’s time window
usmStatsUnknownUserNames
  32-bit Counter
  Number of packets dropped because they referenced an unknown user

## Slide 89: SNMPv3 – VACM MIB
vacmAccessTable
snmpVacm MIB
{.iso.org.dod.internet.snmpV2.snmpModules 16}
VacmMIBObjects
{snmpVacmMIB 1}
vacmContextTable
vacmSecurityToGroupTable
vacmMIBViews
vacmSecurityModel
vacmSecurityName
vacmGroupName
vacmSecurityToGroupStorageType
vacmSecurityToGroupStatus
vacmAccessContextPrefix
vacmAccessSecurityModel
vacmAccessSecurityLevel
vacmAccessContextMatch
vacmAccessReadViewName
vacmAccessWriteViewName
vacmAccessNotifyViewName
vacmContextName
vacmAccessStorageType
vacmAccessStatus
vacmMIBViews
vacmViewTreeFamilyViewName
vacmViewTreeFamilySubtree
vacmViewTreeFamilyMask
vacmViewTreeFamilyType
vacmViewTreeFamilyStorageType
vacmViewTreeFamilyStatus
vacmViewSpinLock

## Slide 90: SNMPv3 - VACM MIB
securityModel
securityName
contextName
vacmSecurityToGroupTable
vacmContextTable
securityLevel
viewType
(read/write/notify)
Object-type
Object-instance
vacmViewTreeFamilyTable
Allow/Deny Access
OID
groupName
viewName
vacmAccessTable
securityModel
WHO
WHERE
HOW
WHY
WHAT
WHICH

## Slide 91: SNMPv3 – VACM Call Flow
securityModel
securityName
contextPrefix
Access type (read, write, notify)
MIB View
Object Identifier
groupName
vacmSecurityTo
GroupTable
vacmAccessTable
vacmViewTree
FamilyTable
securityLevel

## Slide 92: VACM MIB
vacmSecurityToGroupTable indexed by vacmSecurityModel.vacmSecurityName
Object | Type | Access
vacmSecurityModel | SnmpSecurityModel | not-accessible
vacmSecurityName | SnmpAdminString | not-accessible
vacmGroupName | SnmpAdminString | read-create
vacmSecurityToGroupStorageType | StorageType | read-create
vacmSecurityToGroupStatus | RowStatus | read-create

## Slide 93: VACM MIB
vacmAccessTable indexed by
vacmGroupName.vacmAccessContextPrefix.vacmAccessSecurityModel.vacmAccessSecurityLevel
Object | Type | Access
vacmAccessContextPrefix | SnmpAdminString | not-accessible
vacmAccessSecurityModel | SnmpSecurityModel | not-accessible
vacmAccessSecurityLevel | SnmpSecurityLevel | not-accessible
vacmAccessContextMatch | INTEGER | read-create
vacmAccessReadViewName | SnmpAdminString | read-create
vacmAccessWriteViewName | SnmpAdminString | read-create
vacmAccessNotifyViewName | SnmpAdminString | Read-create
vacmAccessStorageType | Storage Type | read-create

## Slide 94: VACM MIB
vacmViewTreeFamilyTable indexed by
vacmViewTreeFamilyViewName.vacmViewTreeFamilySubtree
Object | Type | Access
vacmViewTreeFamilyViewName | SnmpAdminString | not-accessible
vacmViewTreeFamilySubtree | OBJECT IDENTIFIER | not-accessible
vacmViewTreeFamilyMask | OCTET STRING | not-accessible
vacmViewTreeFamilyType | INTEGER {included (1), excluded (2)} | read-create
vacmViewTreeFamilyStorageType | StorageType | read-create
vacmViewTreeFamilyStatus | RowSatus | read-create

## Slide 95: VACM – Status Codes
Status Codes returned by the VACM subsystem
Code | Description | Error Status
accessAllowed | A MIB view was found, access granted | 
notInView | A MIB view found, but access denied | Get: ‘noSuchInstance’ exception Set: ‘noAccess’ error status
noSuchView | No MIB view was found in vacmAccessTable | ‘authorizationError’ error status
noSuchContext | The contextName was not found in vacmContextTable | No response PDU generated Increment ‘snmpUnknownContexts’
noGroupName | The securityName and securityModel could not be mapped into a groupName | ‘authorizationError’ error status
noAccessEntry | A row could not be found in vacmAccessTable | ‘authorizationError’ error status
otherError | Some other undefined error occurred | ‘genError’ error status

## Slide 96: VACM – Example Configuration
Example vacmSecurityToGroupTable Configuration
 | 3.initial
vacmSecurityModel | 3 (USM)
vacmSecurityName | “initial”
vacmGroupName | “initial”
vacmSecurityToGroupStorageType | nonVolatile
vacmSecurityToGroupStatus | active

## Slide 97: VACM – Example Configuration
Example vacmAccessTable Configuration
 | initial.3.1 | initial.3.2 | initial.3.3
vacmGroupName | initial | initial | initial
vacmAccessContextPrefix | “” | “” | “”
vacmAccessSecurityModel | 3 (USM) | 3 (USM) | 3 (USM)
vacmAccessSecurityLevel | 1 (noAuthNoPriv) | 2 (AuthNoPriv) | 3 (AuthPriv)
vacmAccessContextMatch | exact | exact | exact
vacmAccessReadViewName | restricted | internet | internet
vacmAccessWriteViewName | “” | internet | internet
vacmAccessNotifyViewName | restricted | internet | internet

## Slide 98: VACM – Example Configuration
Example vacmViewTreeFamily for mimimum security
 | internet.1.3.6.1 | restricted.1.3.6.1
vacmViewTreeFamilyViewName | internet | restricted
vacmViewTreeFamilySubtree | 1.3.6.1 | 1.3.6.1
vacmViewTreeFamilyMask | “” | “”
vacmViewTreeFamilyType | 1 (included) | 1 (included)
vacmViewTreeFamilyStorageType | nonVolatile | nonVolatile
vacmViewTreeFamilyStatus | active | active

## Slide 99: VACM – Example Configuration
Example vacmViewTreeFamily for semi-secure configuration
 | internet.1.3.6.1 | restricted.1.3.6.1.2.1.1
vacmViewTreeFamilyViewName | internet | restricted
vacmViewTreeFamilySubtree | 1.3.6.1 | 1.3.6.1.2.1.1
vacmViewTreeFamilyMask | “” | “”
vacmViewTreeFamilyType | 1 (included) | 1 (included)
vacmViewTreeFamilyStorageType | nonVolatile | nonVolatile
vacmViewTreeFamilyStatus | active | active