## Slide 1: SNMPv3 MIBs

## Slide 2: SNMPv3 MIBs
snmpModules
{snmpV2 3}
snmpMPDMIB
{snmpModules 11}
snmpUSMMIB
{snmpModules 15}
snmpTargetMIB
{snmpModules 12}
snmpFrameworkMIB
{snmpModules 10}
snmpNotificationMIB
{snmpModules 13}
snmpProxyMIB
{snmpModules 14}
snmpVACMMIB
{snmpModules 16}
snmpV2
{internet 6}
internet
{.iso.org.dod.1}

## Slide 3: SNMPv3 – Framework MIB
snmpEngine
snmpEngineID
{snmpEngine 1}
snmpEngineTime
{snmpEngine 3}
snmpEngineBoots
{snmpEngine 2}
snmpEngineMaxMessageSize
{snmpEngine 4}
snmpFrameworkAdmin
{snmpFrameworkMIB 1}
snmpFramework MIB
{.iso.org.dod.internet.snmpV2.snmpModules 10}
snmpFrameworkMIBObjects
snmpFrameworkMIBConformances
{snmpFrameworkMIB 2}
{snmpFrameworkMIB 3}

## Slide 4: Framework MIB
snmpEngineID OBJECT-TYPE
SYNTAX SnmpEngineID
MAX-ACCESS read-only
STATUS current
DESCRIPTION "An SNMP engine's administratively-unique identifier. This information SHOULD be stored in non-volatile storage so that it remains constant across re-initializations of the SNMP engine. "
::= { snmpEngine 1 }
snmpEngineBoots OBJECT-TYPE
SYNTAX INTEGER (1..2147483647)
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The number of times that the SNMP engine has initialized itself since snmpEngineID was last configured. "
::= { snmpEngine 2 }

## Slide 5: Framework MIB
snmpEngineTime OBJECT-TYPE
SYNTAX INTEGER (0..2147483647)
UNITS "seconds"
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The number of seconds since the value of the snmpEngineBoots object last changed. When incrementing this object's value would cause it to exceed its maximum, snmpEngineBoots is incremented as if a re-initialization had occurred, and this object's value consequently reverts to zero. "
::= { snmpEngine 3 }
snmpEngineMaxMessageSize OBJECT-TYPE
SYNTAX INTEGER (484..2147483647)
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The maximum length in octets of an SNMP message which this SNMP engine can send or receive and process, determined as the minimum of the maximum message size values supported among all of the transports available and supported by the engine. "
::= { snmpEngine 4 }

## Slide 6: SNMPv3 – MPD MIB
snmpMPDStats
snmpInvalidMsgs
{snmpMPDStats 2}
snmpUnknownSecurityModels
{snmpMPDStats 1}
snmpUnknownPDUHandlers
{snmpMPDStats 3}
snmpMPDAdmin
{snmpMPDMIB 1}
snmpMPD MIB
{.iso.org.dod.internet.snmpV2.snmpModules 11}
snmpMPDMIBObjects
snmpMPDMIBConformances
{snmpMPDMIB 2}
{snmpMPDMIB 3}

## Slide 7: SNMPv3 – MPD Statistics
snmpUnknownSecurityModels OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The total number of packets received by the SNMP engine which were dropped because they referenced a securityModel that was not known to or supported by the SNMP engine. "
::= { snmpMPDStats 1 }
snmpInvalidMsgs OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The total number of packets received by the SNMP engine which were dropped because there were invalid or inconsistent components in the SNMP message. "
::= { snmpMPDStats 2 }
snmpUnknownPDUHandlers OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION "The total number of packets received by the SNMP engine which were dropped because the PDU contained in the packet could not be passed to an application responsible for handling the pduType, e.g. no SNMP application had registered for the proper combination of the contextEngineID and the pduType. “
::= { snmpMPDStats 3 }

## Slide 8: SNMPv3 Authentication & Privacy MIBs
snmpModules
{snmpV2 3}
snmpMPDMIB
{snmpModules 11}
snmpUSMMIB
{snmpModules 15}
snmpTargetMIB
{snmpModules 12}
snmpFrameworkMIB
{snmpModules 10}
snmpNotificationMIB
{snmpModules 13}
snmpProxyMIB
{snmpModules 14}
snmpVACMMIB
{snmpModules 16}
snmpV2
{internet 6}
internet
{.iso.org.dod.1}

## Slide 9: SNMPv3 – USM MIB
usmUser
snmpUsm MIB
{.iso.org.dod.internet.snmpV2.snmpModules 15}
usmMIBObjects
usmMIBConformances
{snmpUsmMIB 1}
{snmpUsmMIB 2}
usmStats
usmUserSecurityName
usmUserCloneFrom
usmUserAuthProtocol
usmUserAuthKeyChange
usmUserOwnAuthKeyChange
usmUserPrivProtocol
usmUserPrivKeyChange
usmUserOwnPrivKeyChange
usmUserPublic
usmUserSpinLock
usmUserTable
usmUserStorageType
usmUserEngineID
usmStatsDecryptionErrors
usmUserStatus
usmStatsUnsupportedSecLevels
usmStatsNotInTimeWindows
usmStatsUnknownUserNames
usmStatsUnknownEngineIDs
usmStatsWrongDigests

## Slide 10: SNMPv3 – USM MIB
Defines a table of valid users for the User-based Security Model (usmUserTable)
Defines authentication and privacy protocols
Defines USM Error Statistics
A TestAndIncr object, ‘usmUserSpinLock’, used to coordinate ‘set’ operations to the usmUserTable

## Slide 11: SNMPv3 – USM MIB
usmUserAuthProtocol values defined so far:
Authentication Protocol | Value | Object Identifier
None | usmNoAuthProtocol | {snmpAuthProtocols 1}
HMAC-MD5-96 | usmHMACMD5AuthProtocol | {snmpAuthProtocols 2}
HMAC-SHA-96 | usmHMACSHAAuthProtocol | {snmpAuthProtocols 3}

## Slide 12: SNMPv3 – USM MIB
usmUserPrivProtocol values defined so far:
Authentication Protocol | Value | Object Identifier
None | usmNoPrivProtocol | {snmpPrivProtocols 1}
CBC-DES | usmDESPrivProtocol | {snmpPrivProtocols 2}

## Slide 13: SNMPv3 – USM User Table
Object
Type
Access
usmUserEngineID
usmUserName
usmUserSecurityName
usmUserCloneFrom
usmUserAuthProtocol
usmUserAuthKeyChange
usmUserOwnAuthKeyChange
usmUserPrivProtocol
usmUserPrivKeyChange
usmUserOwnPrivKeyChange
usmUserPublic
usmUserStorageType
usmUserStatus
SnmpEngineID
SnmpAdminString
SnmpAdminString
RowPointer
AutonomousType
KeyChange
KeyChange
KeyChange
KeyChange
AutonomousType
OCTET STRING
StorageType
RowStatus
not-accessible
not-accessible
read-only
read-create
read-create
read-create
read-create
read-create
read-create
read-create
read-create
read-create
read-create

## Slide 14: SNMPv3 – USM User Table
‘usmUserTable’ maintains authentication and privacy information for each user
Each user is indexed by an SNMP engine identifier and a user name
The SNMP engine identifier is mostly local but remote engine identifiers can exist
Each row specifies the authentication protocol and the encryption protocol to use when exchanging SNMP messages for a specific user
Each row also contains authentication and encryption KeyChange objects to allow secret keys to be changed remotely

## Slide 15: SNMPv3 – USM User Table
New rows in the usmUserTable are created by cloning them from existing rows
Atleast one template row must be created and have its secret keys configured through some means other than SNMP (through a command line interface) so that the new rows can be cloned from it.

## Slide 16: SNMPv3 – USM Error Statistics
usmStatsUnsupportedSecLevels
  32-bit Counter
  Number of packets dropped because of the requested security level is not supported.
usmStatsNotInTimeWindows
  32-bit Counter
  Number of packets dropped because they were outside an authoritative engine’s time window
usmStatsUnknownUserNames
  32-bit Counter
  Number of packets dropped because they referenced an unknown user

## Slide 17: SNMPv3 MIBs for Configuring Notifications and Proxy Forwarding
snmpModules
{snmpV2 3}
snmpMPDMIB
{snmpModules 11}
snmpUSMMIB
{snmpModules 15}
snmpTargetMIB
{snmpModules 12}
snmpFrameworkMIB
{snmpModules 10}
snmpNotificationMIB
{snmpModules 13}
snmpProxyMIB
{snmpModules 14}
snmpVACMMIB
{snmpModules 16}
snmpV2
{internet 6}
internet
{.iso.org.dod.1}

## Slide 18: MIB Tables for Configuring Notifications and Proxy Forwarding
Management Target MIB
  snmpTargetAddrTable
  snmpTargetParamsTable
Notification MIB
  snmpNotifyTable
  snmpNotifyFilterProfileTable
  snmpNotifyFilterTable
Proxy MIB
  snmpProxyTable

## Slide 19: Management Target MIB
“snmpTargetAddrTable” defines target addresses for generating notifications and proxy forwarding.
  Each row contains an identifier into a parameters table which defines SNMPv3 parameters to use in generating a message.
  Each row contains a list of tag values used by the notification and proxy tables

## Slide 20: SNMPv3 – Target MIB
snmpUnavailableContexts
snmpTarget MIB
{.iso.org.dod.internet.snmpV2.snmpModules 12}
snmpTargetObjects
snmpTargetConformance
{snmpTargetMIB 1}
{snmpTargetMIB 3}
snmpTargetSpinLock
snmpTargetAddrTable
snmpTargetParamsTable
snmpUnknownContexts
snmpTargetAddrName
snmpTargetAddrTDomain
snmpTargetAddrTAddress
snmpTargetAddrTimeout
snmpTargetAddrRetryCount
snmpTargetAddrTagList
snmpTargetAddrParams
snmpTargetAddrStorageType
snmpTargetAddrRowStatus
snmpTargetParamsName
snmpTargetParamsMPModel
snmpTargetParamsSecurityModel
snmpTargetParamsSecurityName
snmpTargetParamsSecurityLevel
snmpTargetParamsStorageType
snmpTargetParamsRowStatus

## Slide 21: Management Target MIB
Object | Type | Access
snmpTargetAddrName | SnmpAdminString | not-accessible
snmpTargetAddrTDomain | TDomain | read-create
snmpTargetAddrTAddress | TAddress | read-create
snmpTargetAddrTimeout | TimeInterval | read-create
snmpTargetAddrRetryCount | Integer32 | read-create
snmpTargetAddrTagList | SnmpTagList | read-create
snmpTargetAddrParams | SnmpAdminString | read-create
snmpTargetAddrStorageType | StorageType | read-create
snmpTargetAddrRowStatus | RowStatus | read-create
snmpTargetAddrTable indexed by snmpTargetAddrName

## Slide 22: Management Target MIB
Object | Type | Access
snmpTargetParamsName | SnmpAdminString | not-accessible
snmpTargetParamsMPModel | SnmpMessageProcessingModel | read-create
snmpTargetParamsSecurityModel | SnmpSecurityModel | read-create
snmpTargetParamsSecurityName | SnmpAdminString | read-create
snmpTargetParamsSecurityLevel | SnmpSecurityLevel | read-create
snmpTargetParamsStorageType | StorageType | read-create
snmpTargetParamsRowStatus | RowStatus | read-create
snmpTargetParamsTable indexed by snmpTargetParamsName

## Slide 23: SNMPv3 – Notification MIB
snmpNotificationMIB
{.iso.org.dod.internet.snmpV2.snmpModules 13}
snmpNotifyObjects
snmpNotifyConformances
{snmpNotificationMIB 1}
{snmpNotificationMIB 3}
snmpNotifyTable
snmpNotifyFilterProfileTable
snmpNotifyFilterTable
snmpNotifyName
snmpNotifyTag
snmpNotifyType
snmpNotifyStorageType
snmpNotifyRowStatus
snmpNotifyFilterProfileName
snmpNotifyFilterProfileStorType
snmpNotifyFilterProfileRowStatus
snmpNotifyFilterSubtree
snmpNotifyFilterMask
snmpNotifyFilterType
snmpNotifyFilterStorageType
snmpNotifyFilterRowStatus

## Slide 24: Notification MIB - snmpNotifyTable
Object | Type | Access
snmpNotifyName | SnmpAdminString | not-accessible
snmpNotifyTag | SnmpTagValue | read-create
snmpNotifyType | INTEGER {SNMPv2-Trap (1), Inform (2)} | read-create
snmpNotifyStorageType | StorageType | read-create
snmpNotifyRowStatus | RowStatus | read-create
snmpNotifyTable indexed by snmpNotifyName

## Slide 25: Simple Notification Configuration
Add a single row in the ‘snmpNotifyTable’ to specify SNMPv2-Trap or Inform PDU to be sent.
For that entry assign a tag value, for instance “trap”
For each notification target address add an entry in the ‘snmpTargetAddrTable’ specifying the target domain, target address, SNMP parameters index, and a tag list value of “trap”.
Leave the ‘snmpNotifyFilterProfileTable’ empty.

## Slide 26: Simple Notifications
snmpTargetAddrTable
snmpTargetAddrTAddress.j
Whether to send an
Inform or SNMPv2 PDU
snmpTargetAddrParams.j
value = params
snmpTargetParamsEntry.params
snmpNotifyType.i
Send Notification
snmpTargetParamsTable
Target address
to send
Notification to
{MPModel
SecurityModel
SecurityName
SecuirtyLevel
snmpNotifyTable
tag
1
2
3
1
2

## Slide 27: Notification MIB- snmpNotifyFilterProfileTable
Object | Type | Access
snmpNotifyFilterProfileName | SnmpAdminString | read-create
snmpNotifyFilterProfileStorType | StorageType | read-create
snmpNotifyFilterProfileRowStatus | RowStatus | read-create
snmpNotifyFilterProfileTable indexed by snmpTargetParamsName

## Slide 28: Notification MIB - snmpNotifyFilterTable
Object | Type | Access
snmpNotifyFilterSubtree | OBJECT IDENTIFIER | not-accessible
snmpNotifyFilterMask | OCTET STRING | read-create
snmpNotifyFilterType | INTEGER {included (1), excluded (2)} | read-create
snmpNotifyFilterStorageType | StorageType | read-create
snmpNotifyFilterRowStatus | RowStatus | read-create
snmpNotifyFilterTable indexed by snmpNotifyFilterProfileName.snmpNotifyFilterSubtree

## Slide 29: Filtering Notifications
snmpTargetAddrTable
snmpTargetAddrParams.j
snmpNotifyTable
snmpNotifyTag.*
value = tag
snmpTargetParamsTable
value = params
value = { snmpTargetParamsMPModel,
snmpTargetParamsSecurityModel
snmpTargetParamsSecurityName
snmpTargetParamsSecurityLevel }
snmpNotifyFilterProfileTable
snmpNotifyFilterProfileName.params
value = params
value = p

## Slide 30: Filtering Notifications
snmpNotifyFilterTable
snmpNotifyFilterSubtree.p.subtree
value = subtree
oidmatches
Add matching entry
to collection
snmpNotifyFilterMask.p.subtree
value = mask
compare trap oid against subtree
.
.1.3.6.1.2.1.2.2
included
snmpNotifyFilterType
value = p
Trap OID
Subtree
Mask
1 1 1 1
.1.3.6.1

## Slide 31: Filtering Notifications
snmpNotifyFilterTable
snmpNotifyFilterSubtree.p.subtree
value = subtree
Vbmatches[varbind1]
add matching entries to the
corresponding varbind collections
snmpNotifyFilterMask.p.subtree
value = mask
compare against each varbind
Vbmatches[varbindn]
Varbind

## Slide 32: SNMPv3 – Proxy MIB
snmpProxyMIB
{.iso.org.dod.internet.snmpV2.snmpModules 14}
snmpProxyObjects
snmpProxyConformances
{snmpProxyMIB 1}
{snmpProxyMIB 2}
snmpProxyName
snmpProxyType
snmpProxyContextEngineID
snmpProxyContextName
snmpProxyTargetParamsIn
snmpProxySingleTargetOut
snmpProxyMultipleTargetOut
snmpProxyStorageType
snmpProxyRowStatus
snmpProxyTable

## Slide 33: Proxy MIB
snmpProxyTable indexed by snmpProxyName
Object | Type | Access
snmpProxyName | SnmpAdminString | not-accessible
snmpProxyType | INTEGER { read (1), write (2), trap (3), inform (4) } | read-create
snmpProxyContextEngineID | snmpEngineID | read-create
snmpProxyContextName | SnmpAdminString | read-create
snmpProxyTargetParamsIn | SnmpAdminString | read-create
snmpProxySingleTargetOut | SnmpAdminString | read-create
snmpProxyMultipleTargetOut | SnmpTagValue | read-create
snmpProxyStorageType | StorageType | read-create
snmpProxyRowStatus | RowStatus | read-create

## Slide 34: Proxy Forwarding
Search ‘snmpProxyTable’ for all entries that matches the incoming message
  ‘snmpProxyContextEngineID’ = ‘contextEngineID’
  ‘snmpProxyContextName’ = ‘contextName (if exists)’
  SNMP parameters match the values referenced by ‘snmpProxyTargetParamsIn’
  Message type matches ‘snmpProxyType’.
If incoming message is a Get, Get-Next, Get-Bulk or Set:
  choose from matching entries whose ‘snmpProxyName’ is smallest.
  Use ‘snmpProxySingleTargetOut’ to determine the target address to forward the incoming message to
If incoming message is a Notification:
  Use each matching entry’s ‘snmpProxyMultipleTargetOut’ value to locate target addresses in the snmpTargetAddrTable.

## Slide 35: How Proxy Forwarding Works
snmpTargetAddrTable
snmpTargetAddrParams.j
snmpProxyTable
snmpProxyMultipleTargetOut
snmpTargetParamsTable
value = params
value = { snmpTargetParamsMPModel,
snmpTargetParamsSecurityModel
snmpTargetParamsSecurityName
snmpTargetParamsSecurityLevel }
contextEngineID
contextName
snmpProxyType
value = tag

## Slide 36: Configuring Proxy Forwarding
Add one or more entries in the snmpTargetAddrTable for the target addresses.
Add one or more row to snmpTargetParamsTable for incoming SNMP parameters.
Add entries to the snmpProxyTable: for read, write, trap and inform requests
  Add contextEngineID of the target device
  Add contextName if applicable

## Slide 37: SNMPv3 – VACM MIB
vacmAccessTable
snmpVacm MIB
{.iso.org.dod.internet.snmpV2.snmpModules 16}
VacmMIBObjects
{snmpVacmMIB 1}
vacmContextTable
vacmSecurityToGroupTable
vacmMIBViews
vacmSecurityModel
vacmSecurityName
vacmGroupName
vacmSecurityToGroupStorageType
vacmSecurityToGroupStatus
vacmAccessContextPrefix
vacmAccessSecurityModel
vacmAccessSecurityLevel
vacmAccessContextMatch
vacmAccessReadViewName
vacmAccessWriteViewName
vacmAccessNotifyViewName
vacmContextName
vacmAccessStorageType
vacmAccessStatus
vacmMIBViews
vacmViewTreeFamilyViewName
vacmViewTreeFamilySubtree
vacmViewTreeFamilyMask
vacmViewTreeFamilyType
vacmViewTreeFamilyStorageType
vacmViewTreeFamilyStatus
vacmViewSpinLock

## Slide 38: SNMPv3 - VACM MIB
securityModel
securityName
contextName
vacmSecurityToGroupTable
vacmContextTable
securityLevel
viewType
(read/write/notify)
Object-type
Object-instance
vacmViewTreeFamilyTable
Allow/Deny Access
OID
groupName
viewName
vacmAccessTable
securityModel
WHO
WHERE
HOW
WHY
WHAT
WHICH

## Slide 39: SNMPv3 – VACM Call Flow
securityModel
securityName
contextPrefix
Access type (read, write, notify)
MIB View
Object Identifier
groupName
vacmSecurityTo
GroupTable
vacmAccessTable
vacmViewTree
FamilyTable
securityLevel

## Slide 40: VACM MIB
vacmSecurityToGroupTable indexed by vacmSecurityModel.vacmSecurityName
Object | Type | Access
vacmSecurityModel | SnmpSecurityModel | not-accessible
vacmSecurityName | SnmpAdminString | not-accessible
vacmGroupName | SnmpAdminString | read-create
vacmSecurityToGroupStorageType | StorageType | read-create
vacmSecurityToGroupStatus | RowStatus | read-create

## Slide 41: VACM MIB
vacmAccessTable indexed by
vacmGroupName.vacmAccessContextPrefix.vacmAccessSecurityModel.vacmAccessSecurityLevel
Object | Type | Access
vacmAccessContextPrefix | SnmpAdminString | not-accessible
vacmAccessSecurityModel | SnmpSecurityModel | not-accessible
vacmAccessSecurityLevel | SnmpSecurityLevel | not-accessible
vacmAccessContextMatch | INTEGER | read-create
vacmAccessReadViewName | SnmpAdminString | read-create
vacmAccessWriteViewName | SnmpAdminString | read-create
vacmAccessNotifyViewName | SnmpAdminString | Read-create
vacmAccessStorageType | Storage Type | read-create

## Slide 42: VACM MIB
vacmViewTreeFamilyTable indexed by
vacmViewTreeFamilyViewName.vacmViewTreeFamilySubtree
Object | Type | Access
vacmViewTreeFamilyViewName | SnmpAdminString | not-accessible
vacmViewTreeFamilySubtree | OBJECT IDENTIFIER | not-accessible
vacmViewTreeFamilyMask | OCTET STRING | not-accessible
vacmViewTreeFamilyType | INTEGER {included (1), excluded (2)} | read-create
vacmViewTreeFamilyStorageType | StorageType | read-create
vacmViewTreeFamilyStatus | RowSatus | read-create

## Slide 43: VACM – Status Codes
Status Codes returned by the VACM subsystem
Code | Description | Error Status
accessAllowed | A MIB view was found, access granted | 
notInView | A MIB view found, but access denied | Get: ‘noSuchInstance’ exception Set: ‘noAccess’ error status
noSuchView | No MIB view was found in vacmAccessTable | ‘authorizationError’ error status
noSuchContext | The contextName was not found in vacmContextTable | No response PDU generated Increment ‘snmpUnknownContexts’
noGroupName | The securityName and securityModel could not be mapped into a groupName | ‘authorizationError’ error status
noAccessEntry | A row could not be found in vacmAccessTable | ‘authorizationError’ error status
otherError | Some other undefined error occurred | ‘genError’ error status

## Slide 44: VACM – Example Configuration
Example vacmSecurityToGroupTable Configuration
 | 3.initial
vacmSecurityModel | 3 (USM)
vacmSecurityName | “initial”
vacmGroupName | “initial”
vacmSecurityToGroupStorageType | nonVolatile
vacmSecurityToGroupStatus | active

## Slide 45: VACM – Example Configuration
Example vacmAccessTable Configuration
 | initial.3.1 | initial.3.2 | initial.3.3
vacmGroupName | initial | initial | initial
vacmAccessContextPrefix | “” | “” | “”
vacmAccessSecurityModel | 3 (USM) | 3 (USM) | 3 (USM)
vacmAccessSecurityLevel | 1 (noAuthNoPriv) | 2 (AuthNoPriv) | 3 (AuthPriv)
vacmAccessContextMatch | exact | exact | exact
vacmAccessReadViewName | restricted | internet | internet
vacmAccessWriteViewName | “” | internet | internet
vacmAccessNotifyViewName | restricted | internet | internet

## Slide 46: VACM – Example Configuration
Example vacmViewTreeFamily for mimimum security
 | internet.1.3.6.1 | restricted.1.3.6.1
vacmViewTreeFamilyViewName | internet | restricted
vacmViewTreeFamilySubtree | 1.3.6.1 | 1.3.6.1
vacmViewTreeFamilyMask | “” | “”
vacmViewTreeFamilyType | 1 (included) | 1 (included)
vacmViewTreeFamilyStorageType | nonVolatile | nonVolatile
vacmViewTreeFamilyStatus | active | active

## Slide 47: VACM – Example Configuration
Example vacmViewTreeFamily for semi-secure configuration
 | internet.1.3.6.1 | restricted.1.3.6.1.2.1.1
vacmViewTreeFamilyViewName | internet | restricted
vacmViewTreeFamilySubtree | 1.3.6.1 | 1.3.6.1.2.1.1
vacmViewTreeFamilyMask | “” | “”
vacmViewTreeFamilyType | 1 (included) | 1 (included)
vacmViewTreeFamilyStorageType | nonVolatile | nonVolatile
vacmViewTreeFamilyStatus | active | active